Appendix B : Logical Data Model / Functional Structure of Information to be Exchanged

This page intentionally left blank

# Table of Contents

Introduction	Error! Bookmark not defined.

REPRESENTATION OF IE	2

IE001. AAR  C_AAR_SND	Error! Bookmark not defined.

IE002. AAR request  C_AAR_REQ	11

IE003. AAR response  C_AAR_RSP	12

IE004. Amendment Acceptance  E_AMD_ACC	13

IE005. Amendment rejection  E_AMD_REJ	14

IE006. Arrival Advice  C_ARR_ADV	15

IE007. Arrival notification  E_ARR_NOT	16

IE008. Arrival notification rejection  E_ARR_REJ	18

IE009. Cancellation decision  E_CAN_DEC	19

IE010. Cancellation notification  C_CAN_NOT	20

IE011. Sensitive GOODs notification  C_SGI_NOT	21

IE013. Declaration amendment  E_DEC_AMD	22

IE014. Declaration cancellation request  E_DEC_CAN	23

IE015. Declaration data  E_DEC_DAT	24

IE016. Declaration rejected  E_DEC_REJ	30

IE017. Departure control results  N_DEP_CON	31

IE018. Destination control results (type A or B)  C_DES_CON	37

IE019. Discrepancies  E_DIS_SND	40

IE020. Discrepancies solved notification  C_DIS_SOL	41

IE021. AAR rejection notification  E_REJ_NOT	42

IE023. guarantor notification  E_gua_NOT	43

IE024. Forwarded arrival advice  (and closing movements) C_FWD_ARR	44

IE025. Goods release notification  E_GDS_REL	45

IE026. Guarantee access codes  E_ACC_COD	46

IE027. Movement query  C_MVT_QUE	47

IE028. MRN Allocated  E_MRN_ALL	48

IE029. Release for Transit  E_REL_TRA	49

IE030. Notification of Customs Offices modification to Common Domain  C_COL_COM	50

IE031. Notification of Customs Offices modification to National Domain  C_COL_NAT	53

IE032. Notification of Common Reference Data modification to National Domain  C_REF_MOD	54

IE034. Query on guarantees  C_GUA_QUE	62

IE035. Recovery notification  E_REC_NOT	63

IE037. Response query on guarantees  C_GUA_RSP	64

IE038. Response to Movement query  C_MVT_RSP	67

IE043. Unloading permission  E_ULD_PER	69

IE044. Unloading Remarks  E_ULD_REM	72

IE045. Write-off notification  E_WRT_NOT	74

IE050. ATR  C_ATR_SND	75

IE051. No release for Transit  E_REL_NOT	76

IE054. Request of release  E_REQ_REL	77

IE055. Guarantee not valid  E_GUA_INV	78

IE058. Unloading remarks rejection  E_ULD_REJ	79

IE059. CANCEL ENQUIRY NOTIFICATION  C_CAN_ENQ	80

IE060. Control decision notification  E_CTR_DEC	81

IE062. Release request rejection  E_REQ_REJ	82

IE063. recovery communication C_REC_COM	83

IE070. Notification of System Unavailability to Common Domain  C_UNA_COM	84

IE071. Notification of System Unavailability to National Domain  C_UNA_NAT	85

IE100. Ask for documents  E_ASK_DOC	86

IE101. Return documents  E_DOC_SND	87

IE102. Request on non-arrived movement  E_REQ_MOV	88

IE103. Information about non-arrived movement  E_MOV_RSP	89

IE104. Enquiry Request  C_ENQ_REQ	90

IE105. Enquiry Reminder  C_ENQ_REM	91

IE106. Enquiry response  C_ENQ_NEG	92

IE110. Paper control results  C_RES_PAP	93

IE111. Authorised consignee query  C_AUT_QUE	94

IE112. Response to Authorised consignee query C_AUT_RSP	95

IE114. ATR Request  C_ATR_REQ	96

IE115. ATR Response  C_ATR_RSP	97

IE118. NCF  C_NCF_NOT	98

IE119. DEPARTURE control DOCUMENT on paper  E_DEP_PAP	100

IE120. DESTINATION control DOCUMENT on paper  E_DES_PAP	101

IE140 Request on non-arrived movement  E_REQ_MOV	102

IE141 Information about non-arrived movement  E_MOV_RSP	103

IE142 Enquiry Request C_ENQ_REQ	104

IE143 Enquiry response C_ENQ_NEG	105

IE144 Enquiry & Recovery Information C_ENR_INF	106

IE145 Enquiry & REcovery Information Request C_INF_REQ	107

IE150 Recovery Request C_REC_REQ	108

IE151 Recovery Acceptance Notification C_REC_ACC	109

IE152 Recovery Dispatch Notification C_REC_DIS	110

IE200. Guarantee check  C_GUA_CHE	111

IE201. Guarantee check result  C_GUA_RES	112

IE203. Guarantee use  C_GUA_USE	113

IE204. Guarantee use cancellation  C_GUA_CAN	114

IE205. Guarantee use result  C_GUA_USR	115

IE209. credit reference amount  C_GUA_Cre	116

IE224. individual guarantee voucher sold  E_igv_INF	117

IE225. Guarantee update notification  E_GUA_WUP	118

IE228. Comprehensive guarantee cancellation liability liberation  E_GOG_CNL	119

IE229. individual guarantee voucher revocation notification  E_IGV_RNG	120

IE231. Comprehensive guarantee cancellation notification  E_COG_CNP	121

IE410. Request for statistics  C_STA_REQ	122

IE411. Sending of statistics data  C_STA_SND	123

IE412. Statistics generated sent to National Domain  C_STA_GEN	124

IE413. OTS statistics sending to Common Domain  C_STA_OTS	125

CONDITIONS FOR IE	126

STRUCTURE RULES	136

5

# Introduction

This chapter aims to describe the detailed structure of each information to be exchanged (IE) identified in Section II - ‘Business Process Threads for Core business’, Section III - ‘Business Process Threads for Guarantee Management’, Section IV - ‘Business Process Threads for Central Services’ and Section V - ‘Business Process Threads for System Administration’.

The ‘Structure of the IE’ is the model used to describe the content of the information to be exchanged between locations.

In this model, IE’s are organised into data groups which contain data (attributes). A data group is not necessarily the equivalent of a database entity. The data (attributes) is grouped together in such a way that they build up coherent logical blocks within the scope of each IE.

The model allows to identify:

- the characteristics of the data groups belonging to the IE: sequence, number of repetitions, a status value to indicate if the data group is mandatory, optional or conditional;

- the characteristics of the data belonging to a data group : sequence, number of repetitions, type, length and a value to indicate if the data is mandatory, optional or conditional;

- data group indentation indicates that the data group may contain not only data but also other groups of data;

- the conditions applicable to data or groups of data towards other data or groups of data in the same IE;

- the structure rules applicable to data or groups of data, explaining how the data or data group in question is used in the IE.

# REPRESENTATION OF IE

# IE015. Declaration data  E_DEC_DAT

TRANSIT OPERATION	1 x	R

TRADER Consignee (Box 8)	1 x 	O	Rule 11

GOODS ITEM	999 x	R	Rule 95

TRADER Consignee (ex Box 8)	1 x 	O	Rule 11

CONTAINERS (Box 31)	99 x	C	Cond55

PACKAGES (Box 31)	99 x	O

TRADER Authorised Consignee (Box 53)	1 x	O	Rule 15

CONTROL RESULT (Box D)	1 x	O

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	C	Cond 85

VALIDITY LIMITATION	99 x	O

# TRANSIT OPERATION

LRN					R	an..22

Declaration type (box 1)			R	an..5

Total number of packages (box 6)	C	n..7	Rule 105

# GOODS ITEM

Declaration type (ex box 1)		C	a..5	Cond45

Country of dispatch (ex box 15a)	C	a2	Cond 135

Destination country (ex box 17a)	C	a2	Cond 140

# CONDITIONS FOR IE

C55	: IF ‘Container’ (box 19) = ‘1’
		THEN	‘CONTAINERS (box 31)’ = ‘R’
		ELSE	‘CONTAINERS (box 31)’ = ‘O’.

# RULES FOR IE

R11	: When there is only 1 Consignee declared, the data group ‘TRADER Consignee (box 8)’ on TRANSIT OPERATION level is used. The data group ‘TRADER Consignee (ex box 8)’ on GOODS ITEM level can not be used

The IE model is divided into five parts:

The identification part, each IE is identified by:

- a unique number that consists of the two characters ‘IE’ followed by a maximum of 3 digits;

- a name.

- a unique reference in a one to one relationship with the unique number of the IE; each IE is prefixed with ‘E_’ (external domain), ‘C_’ (common domain) or ‘N_’ (internal);

The structure part provides the following:

- the sequence of the data groups in the IE;

- a data group name;

- a number followed by the character ‘x’ indicating how many times the data group can be  repeated in the IE;

- a value indicating whether the data group is (R)equired, (O)ptional or (C)onditional. When the value is conditional, a reference to the condition which will be described at the end of the model is provided;

- when relevant, a ‘box number’ representing the number of the box on the SAD;

- reference to the condition and or rule applicable to the data;

- data group indentation indicates that the data group depends on lower indent data group.

The ‘data group’ detail part provides for each data (attribute) the following:

- the sequence of the data within the data group;

- a data group name, the same as in the structure part;

- the attribute name within the data group;

- a value indicating whether the data is (R)equired, (O)ptional or (C)onditional. If the value is conditional, reference to the condition which will be described at the end of the model is provided;

- the data type: (a)lphabetic and/or (n)numeric;

- the data length (the optionally 2 dots before the length indicator mean that the data has no fixed length, but it can have up to a number of digits, as specified by the length indicator); it must be noted that the data type / data length of fields representing a date is always ‘n8’ in order to be year 2000 compliant (e.g. 19980220); also, a comma in the data length (e.g. 8,6), means that the attribute can hold decimals, the digit before the comma indicates the total length of the attribute, the digit after the comma indicates the maximum number of digits after the decimal point;

- when relevant, a ‘box number’ representing the number of the box on the SAD;

- a reference to the condition ‘Cond’ and/or to the ‘Rule’ applicable to the data.

The ‘Condition’ part:

lists all conditions applicable to the data or data group towards other data or data group included in the IE. A condition expresses the dependency of an attribute or data group on the content of another attribute or data group within the same IE. The attribute or data group in question can, due to the condition, be rendered (R)equired, (O)ptional or even ‘not be used’ within the IE.

The ‘Rule’ part:

lists all rules applicable to the data or data group, explaining how the data or how the data group in question is used in the IE.

# IE001. AAR  C_AAR_SND

TRANSIT OPERATION	1 x	R	Rule 143

TRADER Consignor (Box 2)	1 x	O	Rule 10

TRADER Consignor - security	1 x	C	Cond 186

Cond 187	TRADER Consignee (Box 8)	1 x	C	Rule 11

Cond 1

TRADER Consignee - security	1 x	C 	Cond 186

Cond 188

TRADER Carrier	1 x	C 	Cond 186						Rule 181

ITINERARY	99 x 	C	Cond 186

Cond 587	GOODS ITEM	999 x	R	Rule 95

TRADER Consignor (ex Box 2)	1 x	O	Rule 10

TRADER Consignor - security	1 x	C 	Cond 186

Cond 187

TRADER Consignee (ex Box 8)	1 x	C	Rule 11

Cond 2

TRADER Consignee - security	1 x	C 	Cond 186

Cond 188	CONTAINERS (Box 31)	99 x	C	Cond 55

PACKAGES (Box 31)	99 x	R

SGI-CODES (Box 31)	9 x	O 	Rule 155

PREVIOUS ADMINISTRATIVE REFERENCES (Box 40)	9 x	C	Cond 35

PRODUCED DOCUMENTS/CERTIFICATES (Box 44)	99 x	C	Cond 903

Cond 547

SPECIAL MENTIONS (Box 44)	99 x	O

CUSTOMS OFFICE of Departure (Box C)	1 x	R

TRADER Principal (Box 50)	1 x	R

CUSTOMS OFFICE of Transit (Box 51)	9 x	C	Cond 30

Rule 902	CUSTOMS OFFICE of Destination (Box 53)	1 x	R

TRADER Authorised Consignee (Box 53)	1 x	O 	Rule 15

CONTROL RESULT (Box D)	1 x	R

SEALS INFO (Box D)	1 x	O

SEALS ID (Box D)	9999 x	R

RISK ANALYSIS	999 x	C 	Cond 186

Rule 821

# TRANSIT OPERATION

MRN						R	an18

Declaration type (box 1)			R	an..5	Rule 909

Rule 911

Security					O	n1	Rule 229

Total number of items (box 5)		R	n..5

Total number of packages (box 6)	O	n..7

Commercial Reference Number (box 7)	C	an..70 	Cond 186

Cond 547

Rule 876

Country of dispatch (box 15a)		C	a2     	Cond 135

Destination country (box 17a)		C	a2     	Cond 140

Identity At Departure (box 18)		C	an..27	Cond 5

Rule 35

Identity_At_Departure_LNG		O	a2	Rule 99

Nationality at Departure (box 18)	C	a2	Cond 6

Rule 35

Container (box 19)				R	n1	Rule 230

Nationality crossing border (box 21)	C	a2	Cond 10

Rule 36

Identity Crossing Border (box 21)	C	an..31  	Cond 11

Identity_Crossing_Border_LNG	O	a2	Rule 99

Transport mode at border (box 25)	C	n..2

Cond 599

Conveyance reference number		C	an..35 	Cond 531

Loading place (box 27)			O	an..17 	Cond 191

Unloading place 				C	an..35	Cond 186									Cond 589

Unloading place_LNG			O	a2	Rule 99

Agreed location code(box 30)		C	an..17 	Cond 186									Rule 41

Agreed location of goods (box 30)	C	an..35 	Cond 186									Rule 41

Agreed location of goods_LNG		C	a2 	Cond 186									Rule 99

Authorised location of goods (box 30)	C	an..17 	Cond 186									Rule 41

Customs sub place (box 30)		C	an..17 	Cond 186									Rule 41

Total gross mass 				R	n..11,3

Specific circumstance indicator		C	a1 	Cond 186

Rule 825

Transport charges – Method of payment	C	a1 	Cond 186	Declaration Acceptance date		R	n8

Issuing date					R	n8

NCTS Accompanying Document language code	R	a2

# TRADER Consignor

Name (box 2)				R	an..35

Street and number (box 2)		R	an..35

Country (box 2)				R	a2

Postcode (box 2)				R	an..9

City (box 2)					R	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 2)					O	an..17

# TRADER Consignor - security

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

TIN						C	an..17   	Cond 572

# TRADER Consignee

Name (box 8)				R	an..35

Street and number (box 8)		R	an..35

Country (box 8)				R	a2

Postcode (box 8)				R	an..9

City (box 8)					R	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 8)					O	an..17

# TRADER Consignee - security

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 596

# TRADER Carrier

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

TIN						O	an..17

# ITINERARY

Country of routing code			R	a2

# GOODS ITEM

Declaration type (ex box 1)		C	an..5	Cond 45

Commercial Reference Number (ex box 7)	C	an..70 	Cond 186

Cond 547

Rule 876

Country of dispatch (ex box 15a)	C	a2	Cond 135

Destination country (ex box 17a)	C	a2	Cond 140

Rule 901

Textual Description (box 31)		R	an..280

Textual_Description_LNG		O	a2	Rule 99

Item Number (Box 32)			R	n..5	Rule 5

Rule 7

Commodity code (Box 33)		C	an..6	Cond 15

Rule 470

Gross Mass (box 35)			O	n..11,3

Net Mass (box 38)				O	n..11,3

UN dangerous goods code (ex box 44)	O	an4	Cond 186

Transport charges – Method of payment	C	a1	Cond 186

Cond 576

# TRADER Consignor

Name (ex box 2)				R	an..35

Street and number (ex box 2)		R	an..35

Country (ex box 2)				R	a2

Postcode (ex box 2)			R	an..9

City (ex box 2)				R	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 2)				O	an..17

# TRADER Consignor - security

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond572

TRADER Consignee

Name (ex box 8)				R	an..35

Street and number (ex box 8)		R	an..35

Country (ex box 8)				R	a2

Postcode (ex box 8)			R	an..9

City (ex box 8)				R	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 8)				O	an..17

# TRADER Consignee - security

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 596

# CONTAINERS

Container numbers (Box 31)		R	an..11

# SGI-CODES

Sensitive goods code (Box 31)		O	n..2 	Rule 156

Sensitive Quantity (Box 31)		R	n..11,3

# PACKAGES

Marks & numbers of Packages (Box 31)	C	an..42	Cond 60

Marks_&_numbers_of_Packages_LNG	O	a2	Rule 99

Kind of packages (Box 31)		R	an..3

Number of Packages (Box 31)		C	n..5	Cond 60

Rule 21

Number of Pieces (Box 31)		C	n..5	Cond 60

# PREVIOUS ADMINISTRATIVE REFERENCES

Previous Document Type (Box 40)	R	an..6	Rule 20

Rule 79

Previous Document Reference (Box 40)	R	an..20

Previous_Document_Reference_LNG 	O	a2	Rule 99

Complement of information(Box 40)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

PRODUCED DOCUMENTS/CERTIFICATES

Document Type (Box 44)		R	an..4	Cond 901

Rule 79

Document Reference (Box 44)		C	an..35  	Cond 902

Document_Reference_LNG		O	a2	Rule 99

Complement of information(Box 44)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

# SPECIAL MENTIONS

Additional information id (Box 44)	R	an..5	Rule 80

Export from EC (Box 44)		C	n1	Cond 75

Rule 75

Export from country (Box 44)		C	a2	Cond 75

Rule 75

# CUSTOMS OFFICE of Departure

Reference Number (Box C)		R	an8	Rule 901

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				R	an..35

Street and number (box 50)		R	an..35

Country (box 50)				R	a2

Postcode (box 50)				R	an..9

City (box 50)				R	an..35

NAD_LNG					O	a2	Rule 99

# CUSTOMS OFFICE of Transit

Reference Number (Box 51)		R	an8

Date and Time of arrival			C	n12	Cond 598

Rule 660

# CUSTOMS OFFICE of Destination

Reference Number (Box 53)		R	an8 	Rule 901

Rule 904

Rule 905

# TRADER Authorised Consignee

TIN Authorised Consignee (Box 53)	R	an..17

# CONTROL RESULT

Control result code (box D)		R	an2	Rule 903

Date Limit (box D)			R	n8

# SEALS INFO

Seals Number (box D)			R	n..4

# SEALS ID

Seals Identity (box D)			R	an..20

Seals_Identity_LNG			O	a2	Rule 99

# RISK ANALYSIS

Item Number (Box 32) involved	O	n..5	Rule 824

Risk Analysis result code			R	an..5

Risk Analysis text				O	an..350

Risk_Analysis_LNG			O	a2	Rule 99

# IE002. AAR request  C_AAR_REQ

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

COUNTRY of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# COUNTRY of Departure

Country code				R	a2

# IE003. AAR response  C_AAR_RSP

TRANSIT OPERATION	1 x	O	Rule 215

C_AAR_SND	1 x	O	Rule 215

Rule 821

Rule 846

CUSTOMS OFFICE of Departure	1 x	O	Rule 215

CUSTOMS OFFICE Presentation Office	1 x	R

# TRANSIT OPERATION

MRN						R	an18

AAR rejection reason code		R	n..2

AAR rejection reason			C	an..350	Cond 305

AAR_rejection_reason_LNG		O	a2	Rule 99

# C_AAR_SND

# CUSTOMS OFFICE of Departure

Reference Number				R	an8   	Rule 901

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8  	Rule 901

# IE004. Amendment Acceptance  E_AMD_ACC

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of amendment			R	n8

Amendment acceptance date		R	n8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader principal TIN (Box 50)		O	an..17

Rule 12

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# IE005. Amendment rejection  E_AMD_REJ

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

FUNCTIONAL ERROR 	99x 	O 	Rule 123

# TRANSIT OPERATION

Amendment rejection date		R	n8

MRN                                                                                                  R       an18

Date of amendment			R	n8

Amendment rejection motivation code	O	n1

Amendment rejection motivation text	C	an..350	Cond 310

Amendment_rejection_motivation_text_LNG	O	a2	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN (box 50)		C	an17        Rule 12	Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35	Cond 160

Country (box 50)				C	a2	Cond 160

Postcode (box 50)				C	an..9	Cond 160

City (box 50)				C	an..35	Cond 160

NAD_LNG					O	a2	Rule 99

FUNCTIONAL ERROR

Error type 					R	 n2

Error pointer 				R 	an..210

Error reason 				O 	an..6

Original attribute value 			O 	an..140

# IE006. Arrival Advice  C_ARR_ADV

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Arrival date					R	n8

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE007. Arrival notification  E_ARR_NOT

TRANSIT OPERATION	1 x	R

EN ROUTE EVENT	9 x	O	Rule 240

INCIDENT	1 x	O

TRANSHIPMENT	1 x	O

NEW CONTAINERS	99 x	O

NEW SEALS INFO (Box F)	1 x	O

NEW SEALS ID (Box F)	9999 x	R

CTL_CONTROL	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	O

TRADER At Destination 	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Arrival notification date			R	n8

Arrival notification place			R	an..35

Arrival_notification_place_LNG	O	a2	Rule 99

Arrival Agreed Location Code		C	an..17	Cond 155

Rule 245

Arrival Agreed Location Of Goods	C	an..35	Cond 155

Rule 245

Arrival_Agreed_Location_Of_Goods_LNG	O	a2	Rule 99

Arrival Authorised Location Of Goods	C	an..17	Cond 155

Rule 245

Customs sub place				C	an..17	Cond 155

Rule 245

Dialog language indicator at Destination	O	a2	Rule 101

Simplified procedure flag		R	n1	Rule 230

# EN ROUTE EVENT

Place						R	an..35

Place_LNG					O	a2	Rule 99

Country					R	a2

# INCIDENT

Incident flag					R	n1	Rule 230

Incident information(Box 56)		O	an..350

Incident_information_LNG		O	a2	Rule 99

Endorsement date (Box G)		O	n8

Endorsement authority (Box G)		O	an..35

Endorsement_authority_LNG		O	a2	Rule 99

Endorsement place (Box G)		O	an..35

Endorsement_place_LNG		O	a2	Rule 99

Endorsement Country (Box G)		O	a2

# TRANSHIPMENT

New transport means identity (Box 55)	O	an..27	Rule 190

New_transport_means_identity_LNG	O	a2	Rule 99

New transport means nationality (Box 55)	O	a2	Rule 190

Endorsement date (Box F)		O	n8

Endorsement authority (Box F)		O	an..35

Endorsement_authority_LNG		O	a2	Rule 99

Endorsement place (Box F)		O	an..35

Endorsement_place_LNG		O	a2	Rule 99

Endorsement Country (Box F)		O	a2

# NEW CONTAINERS

New container number (Box 55)	O	an..11	Rule 190

# NEW SEALS INFO

New Seals Number (box D)		R	n..4

# NEW SEALS ID

New Seals Identity (box D)		R	an..20

New_Seals_Identity_LNG		O	a2	Rule 99

# CTL_CONTROL

Already in NCTS				R	n1	Rule 230

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# TRADER At Destination

TIN						C	an..17	Cond 112

Name						C	an..35	Cond 160

Street and number				C	an..35	Cond 160

Country					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE008. Arrival notification rejection  E_ARR_REJ

TRANSIT OPERATION	1 x	R

FUNCTIONAL ERROR 	999x 	O 	Rule 123

# TRANSIT OPERATION

# MRN	R       an18

Arrival Rejection date			R	n8

Arrival Rejection reason			O	an..350

Arrival Rejection_reason_LNG		O	a2	Rule 99

Action to be taken				O	an..350

Action_to_be_taken_LNG		O	a2	Rule 99

FUNCTIONAL ERROR

Error type 					R	 n2

Error pointer 				R 	an..210

Error reason 				O 	an..6

Original attribute value 			O 	an..140

# IE009. Cancellation decision  E_CAN_DEC

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of cancellation request		C	n8	Cond 180

Date of cancellation decision		R	n8

Cancellation initiated by Customs	R	n1	Rule 175

Rule 230

Cancellation Decision			C	n1	Cond 170

Rule 180

Rule 230

Cancellation Justification		C	an..350	Cond 175

Cancellation Justification_LNG		O	a2	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN (Box 50)		C	an..17	Rule 174 									Rule 12	Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# IE010. Cancellation notification  C_CAN_NOT

TRANSIT OPERATION	1 x	R	Rule 173

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE of Destination declared	1 x	R

CUSTOMS OFFICE of Transit declared	9 x	O

# TRANSIT OPERATION

MRN						R	an18

Date of cancellation			R	n8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# CUSTOMS OFFICE of Destination declared

Reference Number				R	an8

# CUSTOMS OFFICE of Transit declared

Reference Number				R	an8

# IE011. Sensitive GOODs notification  C_SGI_NOT

C_AAR_SND	1 x	R

# C_AAR_SND

# IE013. Declaration amendment  E_DEC_AMD

E_DEC_DAT	1 x	R	Rule 115

Rule 520

CTL_CONTROL	1 x	R

# E_DEC_DAT

# CTL_CONTROL

Amendment Type Flag			R	n1	Rule 230

# IE014. Declaration cancellation request  E_DEC_CAN

TRANSIT OPERATION	1 x	R

TRADER Principal	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of cancellation request		R	n8

Cancellation reason			R	an..350

Cancellation_reason_LNG		O	a2	Rule 99

# TRADER Principal

Trader Principal TIN (Box 50)		O	an..17	Rule 174 										Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE015. Declaration data  E_DEC_DAT

TRANSIT OPERATION	1 x	R

TRADER Consignor (Box 2)	1 x	O	Rule 10

TRADER Consignor - security	1 x	C	Cond 186

Cond 187

TRADER Consignee (Box 8)	1 x	C	Rule 11

Cond 1

TRADER Consignee - security	1 x	C 	Cond 186

Cond 188

TRADER Carrier	1 x	C 	Cond 186						Rule 181

ITINERARY	99 x 	C	Cond 186

Cond 587

GOODS ITEM	999 x	R

TRADER Consignor (ex Box 2)	1 x	O	Rule 10

TRADER Consignor - security	1 x	C 	Cond 186

Cond 187

TRADER Consignee (ex Box 8)	1 x	C	Rule 11

Cond 2

TRADER Consignee - security	1 x	C 	Cond 186

Cond 188

CONTAINERS (Box 31)	99 x	C	Cond 55

PACKAGES (Box 31)	99 x	R

SGI-CODES (Box 31)	9 x	O	Rule 155

PREVIOUS ADMINISTRATIVE REFERENCES (Box 40)	9 x	C	Cond 35

PRODUCED DOCUMENTS/CERTIFICATES (Box 44)	99 x	C	Cond 903

Cond 547

SPECIAL MENTIONS (Box 44)	99 x	O

CUSTOMS OFFICE of Departure (Box C)	1 x	R

TRADER Principal (Box 50)	1 x	R

REPRESENTATIVE (Box 50)	1 x	O

CUSTOMS OFFICE of Transit (Box 51)	9 x	C	Cond 30

Rule 902

CUSTOMS OFFICE of Destination (Box 53)	1 x	R

TRADER Authorised Consignee (Box 53)	1 x	O	Rule 15

CONTROL RESULT (Box D)	1 x	O	Rule 160

SEALS INFO (Box D)	1 x	O	Rule 165

SEALS ID (Box D)	9999 x	R

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	C	Cond 85

VALIDITY LIMITATION EC	1 x	O

VALIDITY LIMITATION NON EC	99 x	O

# TRANSIT OPERATION

LRN						R	an..22

Declaration type (box 1)			R	an..5   	Rule 909

Rule 911

Security					O	n1	Rule 229

Total number of items (box 5)		R	n..5

Total number of packages (box 6)	O	n..7	Rule 105

Commercial Reference Number (box 7)	C	an..70 	Cond 186

Cond 547

Rule 876

Country of dispatch (box 15a)		C	a2	Cond 135

Destination country (box 17a)		C	a2	Cond 140

Identity At Departure (box 18)		C	an..27	Cond 5

Rule 35

Identity_At_Departure_LNG		O	a2	Rule 99

Nationality at Departure (box 18)	C	a2	Cond 6

Rule 35

Container (box 19)				R	n1	Rule 230

Nationality crossing border (box 21)	C	a2	Cond 10

Rule 36

Identity Crossing Border (box 21)	C	an..31  	Cond 11

Identity_Crossing_Border_LNG	O	a2	Rule 99

Type of Transport Crossing Border (box 21)	O	n..2

Transport mode at border (box 25)	C	n..2	Cond 599

Inland transport mode (box 26)		O	n..2

Conveyance reference number		C	an..35 	Cond 531

Loading place (box 27)			C	an..17	Cond 191

Unloading place 				C	an..35	Cond 186

Cond 589	Unloading place_LNG			O	a2	Rule 99

Agreed location code(box 30)		C	an..17	Cond 100

Rule 41

Agreed location of goods (box 30)	C	an..35	Cond 100

Rule 41

Agreed location of goods_LNG		O	a2	Rule 99

Authorised location of goods (box 30)	C	an..17	Cond 100

Rule 41

Customs sub place (box 30)		C	an..17	Cond 100

Rule 41

Total gross mass (box 35)		R	n..11,3

Specific circumstance indicator		C	a1 	Cond 186

Rule 825

Transport charges – Method of payment	C	a1 	Cond 186

TAD language code			R	a2

Dialog language indicator at Departure	O	a2	Rule 100

Declaration date (box 50)		R	n8

Declaration place (box 50)		R	an..35

Declaration_place_LNG			O	a2	Rule 99

# TRADER Consignor

Name (box 2)				R	an..35

Street and number (box 2)		R	an..35

Country (box 2)				R	a2

Postcode (box 2)				R	an..9

City (box 2)					R	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 2)					O	an..17

# TRADER Consignor - security

Name						C	an..35	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 572

TRADER Consignee

Name (box 8)				R	an..35

Street and number (box 8)		R	an..35

Country (box 8)				R	a2

Postcode (box 8)				R	an..9

City (box 8)					R	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 8)					O	an..17

# TRADER Consignee - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 596

# TRADER Carrier

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						O	an..17

# ITINERARY

Country of routing code			R	a2

# GOODS ITEM

Declaration type (ex box 1)		C	an..5	Cond 45

Commercial Reference Number (ex box 7)	C	an..70 	Cond 186

Cond 547

Rule 876

Country of dispatch (ex box 15a)	C	a2	Cond 135

Destination country (ex box 17a)	C	a2	Cond 140

Textual Description (box 31)		R	an..280

Textual_Description_LNG		O	a2	Rule 99

Item Number (Box 32)			R	n..5	Rule 5

Rule 7

Commodity code (Box 33)		C	an..8	Cond 15

Rule 60

Rule 470

Gross Mass (box 35)			O	n..11,3	Rule 700

Net Mass (box 38)				O	n..11,3

UN dangerous goods code (ex box 44)	O	an4	Cond 186

Transport charges – Method of payment	C	a1	Cond 186

Cond 576

# TRADER Consignor

Name (ex box 2)				R	an..35

Street and number (ex box 2)		R	an..35

Country (ex box 2)				R	a2

Postcode (ex box 2)			R	an..9

City (ex box 2)				R	an..35

NAD_LNG					O	a2 	Rule 99

TIN (ex box 2)				O	an..17

# TRADER Consignor - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 572

TRADER Consignee

Name (ex box 8)				R	an..35

Street and number (ex box 8)		R	an..35

Country (ex box 8)				R	a2

Postcode (ex box 8)			R	an..9

City (ex box 8)				R	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 8)				O	an..17

# TRADER Consignee - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 596

# CONTAINERS

Container numbers (Box 31)		R	an..11

# SGI-CODES

Sensitive goods code (Box 31)		O	n..2	Rule 156

Sensitive Quantity (Box 31)		R	n..11,3

# PACKAGES

Marks & numbers of Packages (Box 31)	C	an..42	Cond 60

Marks_&_numbers_of_Packages_LNG	O	a2	Rule 99

Kind of packages (Box 31)		R	an..3

Number of Packages (Box 31)		C	n..5	Cond 60

Rule 21

Number of Pieces (Box 31)		C	n..5	Cond 60

# PREVIOUS ADMINISTRATIVE REFERENCES

Previous Document Type (Box 40)	R	an..6	Rule 20	Previous Document Reference (Box 40)	R	an..20

Previous_Document_Reference_LNG	O	a2	Rule 99

Complement of information(Box 40)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

PRODUCED DOCUMENTS/CERTIFICATES

Document Type (Box 44)		R	an..4	Cond 901

Document Reference (Box 44)		C	an..35  	Cond 902

Document_Reference_LNG		O	a2	Rule 99

Complement of information (Box 44)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

SPECIAL MENTIONS	Rule 27

Additional information id (Box 44)	O	an..5

Export from EC (Box 44)		C	n1	Cond 75

Rule 75

Export from country (Box 44)		C	a2	Cond 75

Rule 75

Text (Box 44)				O	an..70

Text_LNG					O	a2	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number (Box C)		R	an8 	Rule 901

# TRADER Principal

Trader Principal TIN (Box 50)		C	an..17	Cond 111
									Cond 236

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 50

Street and number (box 50)		C	an..35 	Cond 50

Country (box 50)				C	a2 	Cond 50

Postcode (box 50)				C	an..9 	Cond 50

City (box 50)				C	an..35 	Cond 50

NAD_LNG					O	a2	Rule 99

# REPRESENTATIVE

Name (box 50)				R	an..35

Representative Capacity (Box 50)	O	a..35

Representative_Capacity_LNG		O	a2	Rule 99

# CUSTOMS OFFICE of Transit

Reference Number (Box 51)		R	an8 	Rule 910

Rule 906

Rule 907

Rule 908

Date and Time of arrival			C	n12

Cond 598

Rule 660

# CUSTOMS OFFICE of Destination

Reference Number (Box 53)		R	an8 	Rule 901

Rule 904									Rule 905

# TRADER Authorised Consignee

TIN Authorised Consignee (Box 53)	R	an..17

# CONTROL RESULT

Control Result Code (box D)		R	an2	Rule 903

Date Limit (box D)			R	n8

# SEALS INFO

Seals Number (box D)			R	n..4

# SEALS ID

Seals Identity (box D)			R	an..20

Seals_Identity_LNG			O	a2	Rule 99

# GUARANTEE

Guarantee Type (box 52)			C	an1	Cond 900

# GUARANTEE REFERENCE

GRN (box 52)				C	an..24	Cond 125

Other Guarantee Reference (box 52)	C	an..35	Cond 130

Rule 900

Access Code				C	an4	Cond 86

# VALIDITY LIMITATION EC

Not Valid For EC (box 52)		R	n1	Rule 230

# VALIDITY LIMITATION NON EC

Not Valid For Other Contracting Parties (box 52)	R	a2	Rule 231

# IE016. Declaration rejected  E_DEC_REJ

TRANSIT OPERATION	1 x	R

FUNCTIONAL ERROR 	999x 	O 	Rule 123

# TRANSIT OPERATION

# LRN                                                                                                    R       an..22

Declaration rejection date		R	n8

Declaration Rejection reason		O	an..350

Declaration_Rejection_reason_LNG	O	a2	Rule 99

FUNCTIONAL ERROR

Error type 					R	 n2

Error pointer 				R 	an..210

Error reason 				O 	an..6

Original attribute value 			O 	an..140

# IE017. Departure control results  N_DEP_CON

TRANSIT OPERATION	1 x	R	Rule 213

CONTROL RESULT (Box D)	1 x	R

SEALS INFO (Box D)	1 x	O

SEALS ID (Box D)	9999 x	R

TRADER Consignor (Box 2)	1 x	O	Rule 10

Rule 157

TRADER Consignor - security	1 x	C	Cond 186

Cond 187	TRADER Consignee (Box 8)	1 x	O	Rule 11

Rule 157

TRADER Consignee - security	1 x	C 	Cond 186

Cond 188

TRADER Carrier	1 x	C 	Cond 186						Rule 181

ITINERARY	99 x 	C	Cond 186

Cond 587

GOODS ITEM	9999 x	O

TRADER Consignor (ex Box 2)	1 x	O	Rule 10

Rule 157	TRADER Consignor - security	1 x	C 	Cond 186

Cond 187

TRADER Consignee (ex Box 8)	1 x	O	Rule 11

Rule 157

TRADER Consignee - security	1 x	C 	Cond 186

Cond 188	CONTAINERS (Box 31)	99 x	O

PACKAGES (Box 31)	99 x	O

SGI-CODES (Box 31)	9 x	O	Rule 157

PREVIOUS ADMINISTRATIVE REFERENCES (Box 40)	9 x	O	Rule 157

PRODUCED DOCUMENTS/CERTIFICATES (Box 44)	99 x	C	Rule 157			Cond 901

Cond 547

SPECIAL MENTIONS (Box 44)	99 x	O	Rule 157

CUSTOMS OFFICE of Transit (Box 51)	9 x	C	Cond 186

Cond 30

Rule 902	CUSTOMS OFFICE of Destination (Box 53)	1 x	O

TRADER Authorised Consignee (Box 53)	1 x	O

RESULTS OF CONTROL	1 x	O	Rule 212

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Declaration type (box 1)			O	an..5 	Rule 902

Security					O	n1	Rule 229

Total number of items (box 5)		O	n..5

Commercial Reference Number (box 7)	O	an..70 		Total number of packages (box 6)	O	n..7

Country of dispatch (box 15a)		O	a2

Destination country (box 17a)		O	a2	Rule 901

Identity At Departure (box 18)		O	an..27	Rule 35

Identity_At_Departure_LNG		O	a2	Rule 99

Nationality at Departure (box 18)	O	a2	Rule 35

Container (box 19)				O	n1	Rule 230

Nationality crossing border (box 21)	O	a2	Rule 36

Identity Crossing Border (box 21)	O	an..31

Identity_Crossing_Border_LNG	O	a2	Rule 99

Type of Transport Crossing Border (box 21)	O	n..2

Transport mode at border (box 25)	O	n..2

Inland transport mode (box 26)		O	n..2

Conveyance reference number		C	an..35	Cond 531

Loading place (box 27)			O	an..17

Unloading place 				O	an..35		Unloading place_LNG			O	a2	Rule 99	Agreed location code(box 30)		O	an..17	Rule 41

Agreed location of goods (box 30)	O	an..35	Rule 41

Agreed location of goods_LNG		O	a2	Rule 99

Authorised location of goods (box 30)	O	an..17	Rule 41

Customs sub place (box 30)		O	an..17	Rule 41

Total gross mass (box 35)		O	n..11,3

Specific circumstance indicator		O	a1

Rule 825

Transport charges – Method of payment	O	a1

Binding itinerary (Box D)		R	n1 	Rule 230

Release requested				O	n1	Rule 230

Release request date			O	n8

Security code				R	an..8

# CONTROL RESULT

Controlled by (Box D)			R	an..35

Controlled_by_LNG			O	a2	Rule 99

Control date (Box D)			R	n8

Control result code (box D)		R	an2	Rule 903

Date Limit (Box D)			R	n8

Remark (Box D)				O	an..350

Remark_LNG				O	a2	Rule 99

# SEALS INFO

Seals Number (box D)			R	n..4

# SEALS ID

Seals Identity (box D)			R	an..20

Seals_Identity_LNG			O	a2	Rule 99

# TRADER Consignor

Name (box 2)				O	an..35

Street and number (box 2)		O	an..35

Country (box 2)				O	a2

Postcode (box 2)				O	an..9

City (box 2)					O	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 2)					O	an..17

# TRADER Consignor - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 572

TRADER Consignee

Name (box 8)				O	an..35

Street and number (box 8)		O	an..35

Country (box 8)				O	a2

Postcode (box 8)				O	an..9

City (box 8)					O	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 8)					O	an..17

# TRADER Consignee - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 596

# TRADER Carrier

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						O	an..17

# ITINERARY

Country of routing code			R	a2

# GOODS ITEM

Declaration type (ex box 1)		O	an..5

Commercial Reference Number (ex box 7)	O	an..70 		Country of dispatch (ex box 15a)	O	a2

Destination country (ex box 17a)	O	a2

Textual Description (Box 31)		O	an..280

Textual_Description_LNG		O	a2	Rule 99

Item Number (Box 32)			R	n..5

Commodity code (Box 33)		O	an..8

Gross Mass (box 35)			O	n..11,3

Net Mass (box 38)				O	n..11,3

UN dangerous goods code (ex box 44)	O	an4

# Transport charges – Method of payment		O	a1

# TRADER Consignor

Name (ex box 2)				O	an..35

Street and number (ex box 2)		O	an..35

Country (ex box 2)				O	a2

Postcode (ex box 2)			O	an..9

City (ex box 2)				O	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 2)				O	an..17

# TRADER Consignor - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 572

TRADER Consignee

Name (ex box 8)				O	an..35

Street and number (ex box 8)		O	an..35

Country (ex box 8)				O	a2

Postcode (ex box 8)			O	an..9

City (ex box 8)				O	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 8)				O	an..17

# TRADER Consignee - security

Name						C	an..35 	Cond 501

Street and number				C	an..35 	Cond 501

Country					C	a2 	Cond 501

Postcode					C	an..9 	Cond 501

City						C	an..35 	Cond 501

NAD_LNG					O	a2	Rule 99

TIN						C	an..17  	Cond 596

# CONTAINERS

Container numbers (Box 31)		R	an..11

Complete Control				R	n1	Rule 230

# SGI-CODES

Sensitive goods code (Box 31)		O	n..2

Sensitive Quantity (Box 31)		O	n..11,3

Complete Control				R	n1	Rule 230

# PACKAGES

Marks & numbers of Packages (Box 31)	O	an..42

Marks_&_numbers_of_Packages_LNG	O	a2	Rule 99

Kind of packages (Box 31)		R	an..3

Number of Packages (Box 31)		O	n..5

Number of Pieces(Box 31)		O	n..5

Complete Control				R	n1	Rule 230

Controlled packages			O	an..70

Controlled_packages_LNG		O	a2	Rule 99

# PREVIOUS ADMINISTRATIVE REFERENCES

Previous Document Type (Box 40)	O	an..6

Previous Document Reference (Box 40)	O	an..20

Previous_Document_Reference_LNG	O	a2	Rule 99

Complement of information (Box 40)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

Complete Control				R	n1	Rule 230

# PRODUCED DOCUMENTS/CERTIFICATES

Document Type (Box 44)		R	an..4	Cond 901

Document Reference (Box 44)		C	an..35  	Cond 902

Document_Reference_LNG		O	a2	Rule 99

Complement of information (Box 44)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

Complete Control				R	n1	Rule 230

# SPECIAL MENTIONS

Additional information id (Box 44)	O	an..5

Export from EC (Box 44)		O	n1	Rule 75

Export from country (Box 44)		O	a2	Rule 75

Text (Box 44)				O	an..70

Text_LNG					O	a2	Rule 99

Complete Control				R	n1	Rule 230

# CUSTOMS OFFICE of Transit

Reference Number (Box 51)		R	an8   	Rule 906			Rule 907			Rule 908			Rule 910

Date and Time of arrival			C	n12

Cond 598

Rule 660

# CUSTOMS OFFICE of Destination

Reference Number (Box 53)		R	an8 	Rule 901

Rule 904

Rule 905

# TRADER Authorised Consignee

TIN Authorised Consignee (Box 53)	R	an..17

# RESULTS OF CONTROL

Control indicator				R	an2

Description					O	an..140

Description_LNG				O	a2	Rule 99

Corrected value				O	xxx	Rule 150

# CUSTOMS OFFICE of Departure

Reference Number (Box C)		R	an8 	Rule 901

# TRADER Principal

Trader Principal TIN (Box 50)		C	an..17	Cond 111

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE018. Destination control results (type A or B)  C_DES_CON

TRANSIT OPERATION	1 x	R

CONTROL RESULT	1 x	R

GOODS ITEM	9999 x	C	Cond 185

Rule 355

CONTAINERS (Box 31)	99 x	C	Cond 185

PACKAGES (Box 31)	99 x	C	Cond 185

SGI-CODES (Box 31)	9 x	C	Cond 185

PRODUCED DOCUMENTS/CERTIFICATES (Box 44)	99 x	C	Cond 185

RESULTS OF CONTROL	1 x	C	Cond 185

Rule 210

EN ROUTE EVENT	9 x	O	Rule 217

INCIDENT	1 x	O

TRANSHIPMENT	1 x	O

NEW CONTAINERS	99 x	O

NEW SEALS INFO (Box F)	1 x	O

NEW SEALS ID (Box F)	9999 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Enquiry engaged at Destination	C	n1	Cond 185

Rule 230

Total number of items (box 5)		C	n..5	Cond 185

Total number of packages (box 6)	C	n..7	Cond 185

Identity At Departure (box 18)		C	an..27	Cond 185

Identity_At_Departure_LNG		O	a2	Rule 99

Nationality at Departure (box 18)	C	a2	Cond 185

Total gross mass (box 35)		C	n..11,3	Cond 185

# CONTROL RESULT

Control date (box I)			R	n8

Control result code (box I)		R	an2

State of seals ok				O	n1	Rule 230

Rule 325

Waiting for discrepancies resolution	C	n1	Cond 90

Rule 230

# GOODS ITEM

Textual Description (Box 31)		O	an..280

Textual_Description_LNG		O	a2	Rule 99

Item Number (Box 32)			R	n..5

Commodity code (Box 33)		C	an..6	Cond 15

Gross Mass (box 35)			O	n..11,3

Net Mass (box 38)				O	n..11,3

# CONTAINERS

Container numbers (Box 31)		R	an..11

# SGI-CODES

Sensitive goods code (Box 31)		O	n..2

Sensitive Quantity (Box 31)		R	n..11,3

# PACKAGES

Marks & numbers of Packages (Box 31)	C	an..42	Cond 60

Marks_&_numbers_of_Packages_LNG	O	a2	Rule 99

Kind of packages (Box 31)		R	an..3

Number of Packages (Box 31)		C	n..5	Cond 60

Rule 21

Number of Pieces (Box 31)		C	n..5	Cond 60

PRODUCED DOCUMENTS/CERTIFICATES

Document Type (Box 44)		R	an..4	Cond 901

Document Reference (Box 44)		C	an..35  	Cond 902

Document_Reference_LNG		O	a2	Rule 99

Complement of information (Box 44)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

# EN ROUTE EVENT

Place						R	an..35

Place_LNG					O	a2	Rule 99

Country					R	a2

# INCIDENT

Incident flag					R	n1	Rule 230

Incident information(Box 56)		O	an..350

Incident_information_LNG		O	a2	Rule 99

Endorsement date (Box G)		O	n8

Endorsement authority (Box G)		O	an..35

Endorsement_authority_LNG		O	a2	Rule 99

Endorsement place (Box G)		O	an..35

Endorsement_place_LNG		O	a2	Rule 99

Endorsement Country (Box G)		O	a2

# TRANSHIPMENT

New Transport Means Identity (Box 55)	O	an..27	Rule 190

New_Transport_Means_Identity_LNG	O	a2	Rule 99

New Transport Means Nationality (Box 55)	O	a2	Rule 190

Endorsement Date (Box F)		O	n8

Endorsement Authority (Box F)		O	an..35

Endorsement_Authority_LNG		O	a2	Rule 99

Endorsement Place (Box F)		O	an..35

Endorsement_Place_LNG		O	a2	Rule 99

Endorsement Country (Box F)		O	a2

# NEW CONTAINERS

New container number (Box 55)	O	an..11	Rule 190

# NEW SEALS INFO

New Seals Number (box F)		R	n..4

# NEW SEALS ID

New Seals Identity (box F)		R	an..20

New_Seals_Identity_LNG		O	a2	Rule 99

# RESULTS OF CONTROL

Control indicator				R	an2

Description					O	an..140

Description_LNG				O	a2	Rule 99

Corrected value				O	an..27	Rule 150

# CUSTOMS OFFICE Presentation Office

Reference Number 			R	an8

# CUSTOMS OFFICE of Departure

Reference Number 			R	an8

# IE019. Discrepancies  E_DIS_SND

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

GUARANTOR	1 x	O

# TRANSIT OPERATION

MRN						R	an18

Discrepancies notification text		O	an..350

Discrepancies_notification_text_LNG	O	a2	Rule 99

Discrepancies notification date		R	n8

# CUSTOMS OFFICE of Departure

Reference Number 			R	an8

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17	Rule 12

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				R	an..35

Street and number (box 50)		R	an..35

Country (box 50)				R	a2

Postcode (box 50)				R	an..9

City (box 50)				R	an..35

NAD_LNG					O	a2	Rule 99

# GUARANTOR

TIN						O	an..17	Rule 12

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# IE020. Discrepancies solved notification  C_DIS_SOL

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Discrepancies solved notification code	R	an..2

Discrepancies solved notification text	O	an..350

Discrepancies_solved_notification_text_LNG	O	a2	Rule 99

Discrepancies solved notification date	R	n8

# CUSTOMS OFFICE of Departure

Reference Number 			R	an8

# CUSTOMS OFFICE Presentation Office

Reference Number 			R	an8

# IE021. AAR rejection notification  E_REJ_NOT

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

TRADER at Destination	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Diversion rejection code			R	n..2

Diversion rejection text			C	an..350	Cond 312

Diversion_rejection_text_LNG		O	a2	Rule 99

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# TRADER at Destination

TIN						O	an..17	Rule 12

Name						C	an..35	Cond 160

Street and number				C	an..35	Cond 160

Country					C	a2	Cond 160

Postcode					C	an..9	Cond 160

City						C	an..35	Cond 160

NAD_LNG					O	a2	Rule 99

# IE023. guarantor notification  E_gua_NOT

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

GUARANTOR	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Declaration Acceptance date		R	n8

Guarantor notification text		O	an..350

Guarantor_notification_text_LNG	O	a2	Rule 99

Guarantor notification date		R	n8

CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17	Rule 12

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				R	an..35

Street and number (box 50)		R	an..35

Country (box 50)				R	a2

Postcode (box 50)				R	an..9

City (box 50)				R	an..35

NAD_LNG					O	a2	Rule 99

COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# GUARANTOR

TIN						O	an..17	Rule 12

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# IE024. Forwarded arrival advice  (and closing movements) C_FWD_ARR

TRANSIT OPERATION	1 x	R	Rule 170

CUSTOMS OFFICE Presentation Office	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE of Destination declared	1 x	R

CUSTOMS OFFICE of Transit declared	9 x	O

# TRANSIT OPERATION

MRN						R	an18

Arrival date					O	n8

# Customs Office Presentation Office

Reference Number				R	an8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# CUSTOMS OFFICE of Destination declared

Reference Number				R	an8

# CUSTOMS OFFICE of Transit declared

Reference Number				R	an8

# IE025. Goods release notification  E_GDS_REL

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

TRADER At Destination	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Release date					R	n8

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# TRADER At Destination

TIN						O	an..17	Rule 12

Name						C	an..35	Cond 160

Street and number				C	an..35	Cond 160

Country					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE026. Guarantee access codes  E_ACC_COD

TRADER Principal	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

GUARANTEE REFERENCE	1 x	R

ACCESS CODE of Principal old	1 x	R

ACCESS CODE of Principal new	1 x	R

ACCESS CODE	99x	O

# TRADER Principal

Trader Principal TIN			R	an..17 	Rule 12

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# GUARANTEE REFERENCE

GRN						R	an..24

# ACCESS CODE of Principal old

Access code					R	an4

# ACCESS CODE of Principal new

Access code					R	an4	Rule 350

# ACCESS CODE

Access code					R	an4

# IE027. Movement query  C_MVT_QUE

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE requester	1 x	R

COUNTRY of Departure	1 x	R

CTL_CONTROL	1 x	O

MOVEMENT QUERY REASON	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE requester

Reference Number				R	an8

# COUNTRY of Departure

Country code				R	a2

# CTL_CONTROL

Other movement information request	O	an..350

Other_movement_information_request_LNG	O	a2	Rule 99

# MOVEMENT QUERY REASON

Movement_Query Reason Code	R	an..3

# IE028. MRN Allocated  E_MRN_ALL

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

LRN						R	an..22

MRN						R	an18

Declaration Acceptance date		R	n8

# CUSTOMS OFFICE Of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN			O	an..17	Rule 12

Holder ID TIR				C	an..17	Cond 904

Name						C	an..35	Cond 160

Street and number				C	an..35	Cond 160

Country					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE029. Release for Transit  E_REL_TRA

E_DEC_DAT	1 x	R	Rule 143

TRANSIT OPERATION	1 x	R

OFFICE TO RETURN COPIES	1 x	O	Rule 330

CONTROL RESULT (Box D)	1 x	O	Rule 335

# E_DEC_DAT

# TRANSIT OPERATION

MRN						R	an18

Issuing Date					R	n8

Declaration Acceptance Date		R	n8

NCTS Return Copy			R	n1	Rule 330

Binding Itinerary (Box D)		R	n1	Rule 230

Authorisation Id				O	an..17

# OFFICE TO RETURN COPIES

Reference Number				R	an8

Customs Office Name			R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# CONTROL RESULT

Controlled By (Box D)			R	an..35

Controlled_By_LNG			O	a2	Rule 99

Control Date (Box D)			R	n8

# IE030. Notification of Customs Offices modification to Common Domain  C_COL_COM

CUSTOMS OFFICE	9999 x	O

ACTION	1 x	R

CUSTOMS OFFICE LSD	9 x	R

CUSTOMS OFFICE ROLE	9 x	R

TRAFFIC COMPETENCE	9 x	R

CUSTOMS OFFICE TIMETABLE	9 x	O	Rule 485

CUSTOMS OFFICE TIMETABLE LINE	9 x	R

CUSTOMS OFFICE SPECIFIC NOTES	99 x	O

TRADER DEDICATED	99 x	O

COUNTRY/REGION	99 x	O

ACTION	1 x	R

COUNTRY/REGION LSD	9 x	R

COUNTRY/REGION HOLIDAYS	99 x	O

COUNTRY/REGION HOLIDAYS LSD	9 x	R

COUNTRY HOLIDAYS	99 x	O

ACTION	1 x	R

COUNTRY HOLIDAYS DATA	99 x	R

COUNTRY HOLIDAYS DATA LSD	9 x	R

# CUSTOMS OFFICE

Reference Number 			R	an8

Reference Number Main Office		O	an8	Rule 489

Reference Number Higher Authority	O	an8	Rule 490

Reference Number Take-Over		O	an8	Rule 495

Reference Number Competent Authority of Enquiry 	O 	an8

Reference Number Competent Authority of Recovery 	O 	an8

Country Code				R	a2

UN/LOCODE				O	a3	Rule 460

Region Code				O	an..3

NCTS Entry Date 				O	n8

Nearest Office				C	an..175	Cond 410

Nearest_Office_LNG			O	a2	Rule 99

Postcode					R	an..9

Phone Number				O	an..35	Rule 500

Fax Number 				O	an..35 	Rule 500

Telex Number 				O	an..35 	Rule 500

E-Mail Address 				O	an..70 	Rule 500

Geo Info Code 				O	an..6

Trader Dedicated				R	n1

# CUSTOMS OFFICE LSD

Language Code				R	a2

Customs Office Usual Name 		R	an..35

Customs_Office_Usual_Name_LNG	O	a2	Rule 99

Street And Number			R	an..35

Street_And_Number_LNG		O	a2	Rule 99

City						R	an..35	Rule 422

City_LNG					O	a2	Rule 99

Prefix-Suffix Level			O	an1

Prefix-Suffix Flag				R	n1

Prefix-Suffix Name			O	an..35

Prefix_Suffix_Name_LNG		O	a2	Rule 99

Space_To_Add				R	n1

# CUSTOMS OFFICE ROLE

Role						R	an..3

# TRAFFIC COMPETENCE

Traffic Type 				R	an..3

# CUSTOMS OFFICE TIMETABLE

Season Code				R	n1	Rule 425

Season Name				O	an..35

Season_Name_LNG			O	a2	Rule 99

Variable Season Date			R	n1	Rule 232

Season Start Day				R	n2	Rule 403

Season Start Month			R	n2	Rule 403

Season Start Year				C	n4	Cond 295

Season End Day				R	n2	Rule 403

Season End Month				R	n2	Rule 403

Season End Year				C	n4	Cond 295

# CUSTOMS OFFICE TIMETABLE LINE

Day In The Week (BEGIN DAY)	R	n1	Rule 430

Opening Hours Time First Period FROM	R	n4

Opening Hours Time First Period TO	R	n4

Day In The Week (END DAY)		R	n1	Rule 430

Opening Hours Time Second Period FROM	O	n4

Opening Hours Time Second Period TO	O	n4

CUSTOMS OFFICE SPECIFIC NOTES

Specific Notes Code			R	an..6	Rule 486

# TRADER DEDICATED

Trader Dedicated Name			R	an..35

Trader_Dedicated_Name_LNG 	O	a2	Rule 99

TIN						O	an..17

# COUNTRY/REGION

Country Code				R	a2

Country/Region Code			R	an..3

# COUNTRY/REGION LSD

Language Code				R	a2	Country/Region Name			R	an..35

Country/Region_Name_LNG		O	a2	Rule 99

# COUNTRY/REGION HOLIDAYS

Variable Holiday Date			R	n1	Rule 232

Day						R	n2

Month					R	n2

Year						C	n4	Cond 295

# COUNTRY/REGION HOLIDAYS LSD

Language Code				R	a2

Public Holiday Name			R	an..35

Public_Holiday_Name_LNG		O	a2	Rule 99

# COUNTRY HOLIDAYS

Country Code				R	a2

# COUNTRY HOLIDAYS DATA

Variable Holiday Date			R	n1	Rule 232

Day						R	n2

Month					R	n2

Year						C	n4	Cond 295

# COUNTRY HOLIDAYS DATA LSD

Language Code				R	a2

Public Holiday Name			R	an..35

Public_Holiday_Name_LNG		O	a2	Rule 99

# ACTION

Operation					R	a1	Rule 410

Validity Date				C	n8	Cond 300

Rule 410

Modification Subtype			C	n1	Cond 300

Rule 410

# IE031. Notification of Customs Offices modification to National Domain  C_COL_NAT

C_COL_COM	1 x	R

# C_COL_COM

# IE032. Notification of Common Reference Data modification to National Domain  C_REF_MOD

INFORMATION RESPONSE	99 x	O

ACTION	1 x	R

INFORMATION RESPONSE LSD	9 x	R

AMENDMENT REJECTION MOTIVATION	9 x	O

ACTION	1 x	R

AMENDMENT REJECTION MOTIVATION LSD	9 x	R

AAR REJECTION REASON	99 x	O

ACTION	1 x	R

AAR REJECTION REASON LSD	9 x	R

ATR REJECTION REASON	99 x	O

ACTION	1 x	R

ATR REJECTION REASON LSD	9 x	R

CONTROL RESULT CODE	99 x	O

ACTION	1 x	R

CONTROL RESULT CODE LSD	9 x	R

RESULTS OF CONTROL	99 x	O

ACTION	1 x	R

RESULTS OF CONTROL LSD	9 x	R

COUNTRY	999 x	O

ACTION	1 x	R

COUNTRY LSD	9 x	R

COUNTRY REGIME	9 x	O

ACTION	1 x	R

COUNTRY REGIME LSD	9 x	R

CUSTOMS OFFICE GEO INFO	99 x	O

ACTION	1 x	R

CUSTOMS OFFICE GEO INFO LSD	9 x	R

CUSTOMS OFFICE SPECIFIC NOTES	99 x	O

ACTION	1 x	R

CUSTOMS OFFICE SPECIFIC NOTES LSD	9 x	R

CURRENCY CODE	99 x	O

ACTION	1 x	R

CURRENCY CODE LSD	9 x	R

DECLARATION TYPE	99 x	O

ACTION	1 x	R

DECLARATION TYPE LSD	9 x	R

DISCREPANCIES SOLVED NOTIFICATION	99 x	O

ACTION	1 x	R

DISCREPANCIES SOLVED NOTIFICATION LSD	9 x	R

DIVERSION REJECTION REASON	99 x	O

ACTION	1 x	R

DIVERSION REJECTION REASON LSD	9 x	R

DOCUMENT TYPE	99 x	O

ACTION	1 x	R

DOCUMENT TYPE LSD	9 x	R

GUARANTEE TYPE	99 x	O

ACTION	1 x	R

GUARANTEE TYPE LSD	9 x	R

GUARANTEE MONITORING	99 x	O

ACTION	1 x	R

GUARANTEE MONITORING LSD	9 x	R

INVALID GUARANTEE REASON	99 x	O

ACTION	1 x	R

INVALID GUARANTEE REASON LSD	9 x	R

LANGUAGE CODE	999 x	O

ACTION	1 x	R

LANGUAGE CODE LSD	9 x	R

PACKAGING CODE	999 x	O

ACTION	1 x	R

PACKAGING CODE LSD	9 x	R

PREVIOUS DOCUMENT TYPE	999 x	O

ACTION	1 x	R

PREVIOUS DOCUMENT TYPE LSD	9 x	R

REQUEST FOR INFORMATION	9 x	O

ACTION	1 x	R

REQUEST FOR INFORMATION LSD	9 x	R

RISK ANALYSIS RESULT CODE	99 x	O

ACTION	1 x	R

REQUEST FOR INFORMATION LSD	99 x	R

ROLE		9 x	O

ACTION	1 x	R

ROLE LSD	9 x	R

SENSITIVE GOODS CODE	99 x	O

ACTION	1 x	R

SENSITIVE GOODS CODE LSD	9 x	R

SPECIAL MENTION CODE	99 x	O

ACTION	1 x	R

SPECIAL MENTION CODE LSD	9 x	R

SPECIFIC CIRCUMSTANCE INDICATOR	99 x	O

ACTION	1 x	R

LANGUAGE SPECIFIC DATA	99 x	R	STATISTICS TYPE	99 x	O

ACTION	1 x	R

STATISTICS TYPE LSD	9 x	R

TRAFFIC TYPE	99 x	O

ACTION	1 x	R

TRAFFIC TYPE LSD	9 x	R

TRANSPORT CHARGES METHOD OF PAYMENT 	99 x	O

ACTION	1 x	R

LANGUAGE SPECIFIC DATA	99 x	R

TRANSIT OPERATION STATE TYPE	99 x	O

ACTION	1 x	R

TRANSIT OPERATION STATE TYPE LSD	9 x	R

UNITS OF MEASURE	99 x	O

ACTION	1 x	R

UNITS OF MEASURE LSD	9 x	R

UN DANGEROUS GOODS CODE 	999 x	O

ACTION	1 x	R

LANGUAGE SPECIFIC DATA	99 x	R	UN/LOCODE	9999 x	O

ACTION	1 x	R

TRANSPORT MODE	99 x	O

ACTION	1 x	R

TRANSPORT MODE LSD	9 x	R

QUERY ON GUARANTEE TYPE	99 x	O

ACTION	1 x	R

QUERY ON GUARANTEE TYPE LSD	9 x	R

# INFORMATION RESPONSE

Information Response Code		R	n2

# INFORMATION RESPONSE LSD

Language code				R	a2

Information Response Name		R	an..70

Information Response_LNG 		O	a2	Rule 99

# AMENDMENT REJECTION MOTIVATION

Amendment Rejection Motivation Code	R	n1

# AMENDMENT REJECTION MOTIVATION LSD

Language code				R	a2

Amendment Rejection Motivation Name	R	an..70

Amendment Rejection Motivation_LNG 	O	a2	Rule 99

# AAR REJECTION REASON

AAR Rejection Reason Code		R	n..2

# AAR REJECTION REASON LSD

Language code				R	a2

AAR Rejection Reason Name		R	an..140

AAR Rejection Reason_LNG 		O	a2	Rule 99

# ATR REJECTION REASON

ATR Rejection Reason Code		R	n..2

# ATR REJECTION REASON LSD

Language code				R	a2

ATR Rejection Reason Name		R	an..140

ATR Rejection Reason_LNG 		O	a2	Rule 99

# CONTROL RESULT CODE

Control Result Code 			R	an2

# CONTROL RESULT CODE LSD

Language Code				R	a2

Control Result Name			R	an..70

Control_Result_Name_LNG 		O	a2	Rule 99

# RESULTS OF CONTROL

Control Indicator				R	an2

# RESULTS OF CONTROL LSD

Language Code				R	a2

Control Indicator Name			R	an..140

Results_Of_Control_Name_LNG	O	a2	Rule 99

# COUNTRY

Country Code				R	a2

TCC Entry Date 				R	n8

NCTS Entry Date 				R	n8

Geo-Nomenclature Code			O	n3

Country Regime Code			R	an3

# COUNTRY LSD

Language Code				R	a2

Country Name				R	an..35

Country_Name_LNG			O	a2	Rule 99

# COUNTRY REGIME

Country Regime Code			R	an3

# COUNTRY REGIME LSD

Language Code				R	a2

Country Regime Name 			R	an..35

Country_Regime_Name_LNG		O	a2	Rule 99

# CUSTOMS OFFICE GEO INFO

Geo Info Code				R	an..6

# CUSTOMS OFFICE GEO INFO LSD

Language Code				R	a2

Geo Info Name				R	an..35

Geo_Info_Name_LNG			O	a2	Rule 99

# CUSTOMS OFFICE SPECIFIC NOTES

Specific Notes Code			R	an..6

# CUSTOMS OFFICE SPECIFIC NOTES LSD

Language Code				R	a2

Specific Notes Code Name		R	an..350

Customs_Office_Specific_Notes_LNG	O	a2	Rule 99

# CURRENCY CODE

Currency					R	an3

Rate Value					R	n..8,6

# CURRENCY CODE LSD

Language code				R	a2

Currency Code Name			R	an..35

Currency_Code_Name_LNG 		O	a2	Rule 99

# DECLARATION TYPE

Declaration Type				R	an..5	Rule 450

# DECLARATION TYPE LSD

Language Code				R	a2

Declaration Type Name			R	an..35

Declaration_Type_Name_LNG		O	a2	Rule 99

# DISCREPANCIES SOLVED NOTIFICATION

Discrepancies Solved Notification Code	R	n..2

# DISCREPANCIES SOLVED NOTIFICATION LSD

Language code				R	a2

Discrepancies Solved Notification Name	R	an..70

Discrepancies Solved Notification_LNG 	O	a2	Rule 99

# DIVERSION REJECTION REASON

Diversion Rejection Reason Code	R	n..2

# DIVERSION REJECTION REASON LSD

Language code				R	a2

Diversion Rejection Reason Name	R	an..140

Diversion Rejection Reason_LNG 	O	a2	Rule 99

# DOCUMENT TYPE

Document Type				R	an..4

# DOCUMENT TYPE LSD

Language Code				R	a2

Document Type Name 			R	an..140

Document_Type_Name_LNG		O	a2	Rule 99

# GUARANTEE TYPE

Guarantee Type				R	an1

# GUARANTEE TYPE LSD

Language Code				R	a2

Guarantee Type Name			R	an.. 140

Guarantee_Type_Name_LNG		O	a2	Rule 99

# GUARANTEE MONITORING

Guarantee Monitoring Code		R	n1

# GUARANTEE MONITORING LSD

Language Code				R	a2

Guarantee Monitoring Description 	R	an..70

Guarantee_Monitoring_Description_LNG	O	a2	Rule 99

# INVALID GUARANTEE REASON

Invalid Guarantee Reason Code 	R	an..3

# INVALID GUARANTEE REASON LSD

Language Code				R	a2

Invalid Guarantee Reason Name	R	an..140

Invalid_Guarantee _Reason_Name_LNG	O	a2	Rule 99

# LANGUAGE CODE

Language Code				R	a2

# LANGUAGE CODE LSD

Language Code				R	a2

Language Code Name			R	an..140

Language_Code_Name_LNG		O	a2	Rule 99

# PACKAGING CODE

Kind of packages				R	an..3	Rule 456

# PACKAGING CODE LSD

Language Code				R	a2

Kind of packages Name 			R	an..140

Kind of packages_Name_LNG		O	a2	Rule 99

Previous Document Type

Previous Document Type (Box 40)	R	an..6	Rule 20

Rule 79

# Previous document type LSD

Language Code				R	a2

Previous document type Name 		R	an..35

Previous document type_Name_LNG	O	a2	Rule 99

# REQUEST FOR INFORMATION

Requested Information Code		R	an..2

# REQUEST FOR INFORMATION LSD

Language code				R	a2

Requested Information Name		R	an..70

Requested Information_LNG 		O	a2	Rule 99

# RISK ANALYSIS RESULT CODE

Risk analysis result Code			R	an1

# RISK ANALYSIS RESULT CODE LSD

Language code				R	a2

Risk analysis result Code	 Name	R	an..140

_ 	Risk analysis result Code_LNG 	O	a2	Rule 99

# ROLE

Role						R	an..3

# ROLE LSD

Language Code				R	a2

Role Description				R	an..70

Role_Description_LNG 			O	a2	Rule 99

# SENSITIVE GOODS CODE

Commodity Code				R	an..6	Rule 445

Sensitive Goods Code			O	n..2	Rule 445

Reference Quantity			O	n..6

Unit of Measure				O	a3

EEC - Territory Limitation		R	n1	Rule 230

# SENSITIVE GOODS CODE LSD

Language Code				R	a2

Sensitive Goods Code Description	R	an..70

Sensitive_Goods_Code_Description_LNG	O	a2	Rule 99

# SPECIAL MENTION CODE

Additional information id		R	an..5	Rule 80

# SPECIAL MENTION CODE LSD

Language Code				R	a2

Additional information id Name	R	an..70

Additional_information_id_Name_LNG	O	a2	Rule 99

# SPECIFIC CIRCUMSTANCE INDICATOR

Specific circumstance indicator		R	a1

# SPECIFIC CIRCUMSTANCE INDICATOR LSD

Language Code				R	a2

Specific circumstance indicator_Name	R	an..35

Specific circumstance indicator_LNG	O	a2	Rule99

STATISTICS TYPE

Statistics Type				R	an3

# STATISTICS TYPE LSD

Language Code				R	a2

Statistics Type Description 		R	an..70

Statistics_Type_Description_LNG 	O	a2	Rule 99

# TRAFFIC TYPE

Traffic Type					R	an..3

# TRAFFIC TYPE LSD

Language Code				R	a2

Traffic Type Description 		R	an..35

Traffic_Type_Description_LNG	O	a2	Rule 99

# TRANSPORT CHARGES METHOD OF PAYMENT

Transport charges / method of payment	R	a1

# TRANSPORT CHARGES METHOD OF PAYMENT LSD

Language Code				R	a2

Transport charges / method of payment_Name	R	an..70

Transport charges / method of payment_LNG	O	a2	Rule 99

# TRANSIT OPERATION STATE TYPE

Transit Operation State Type		R	an..3

# TRANSIT OPERATION STATE TYPE LSD

Language Code				R	a2

Transit Operation State Type Name 	R	an..35

Transit_Operation_State_Type_Name_LNG	O	a2	Rule 99

# UNITS OF MEASURE

Units of Measure Code			R	a3

# UNITS OF MEASURE LSD

Language Code				R	a2

Units of Measure Name			R	an..35

Units_of_Measure_Name_LNG 	O	a2	Rule 99

# UN DANGEROUS GOOD CODE

# UN dangerous goods Code                                                                R       an4	UN

# DANGEROUS GOOD CODE LSD

Language Code				R	a2

UN dangerous goods Code_Name	R	an..35

UN dangerous goods Code_LNG	O	a2

# UN/LOCODE

Country Code				R	a2

UN/LOCODE				R	a3	Rule 460

UN/LOCODE Name			R	a..29	Rule 422

UN/LOCODE LNG			O	a2

# TRANSPORT MODE

Transport Mode				R	n..2

# TRANSPORT MODE LSD

Language Code				R	a2

Transport Mode Description 		R	an..35

Transport_Mode_Description_LNG	O	a2	Rule 99

# QUERY ON GUARANTEE TYPE

Query Identifier 				R	n1

# QUERY ON GUARANTEE TYPE LSD

Language Code				R	a2

Query Identifier Description 		R	an..140

Query_Identifier_Description_LNG	O	a2	Rule 99

# ACTION

Operation					R	a1	Rule 410

Validity Date				C	n8	Cond 300

Rule 410

Modification Subtype			C	n1	Cond 300

Rule 410

Legal References 				O	an..70

Legal_References_LNG 			O	a2	Rule 99	Responsible Data Manager		O	an..35

# IE034. Query on guarantees  C_GUA_QUE

GUARANTEE REFERENCE	99 x	R

GUARANTEE QUERY	1 x	R

TRADER Principal (owner)	1 x	O

ACCESS CODE	1 x	O	Rule 270

AUTHORITY FOR GUARANTEE SIMPLIFICATION	1 x 	O	Rule 265

Rule 266

CUSTOMS OFFICE (requester)	1 x	O 	Rule 265

Rule 266

TRADER Principal (requester)	1 x 	O 	Rule 265

Rule 275

OFFICE OF RECOVERY	1 x	O 	Rule 265

Rule 262

COUNTRY of Guarantee	1 x	C	Cond 227

# GUARANTEE REFERENCE

GRN						R	an..24

# GUARANTEE QUERY

Query identifier				R	n1 	Rule 261

Period from date				O	n8	Rule 263

Period to date				O	n8	Rule 263

# TRADER Principal (owner)

Trader Principal (owner) TIN		R	an..17

# ACCES CODE

Access code					R	an4

# AUTHORITY FOR GUARANTEE SIMPLIFICATION

Reference Number				R	an8

CUSTOMS OFFICE (requester)

Reference Number				R	an8

# TRADER Principal (requester)

Trader Principal (requester) TIN	R	an..17

# OFFICE OF RECOVERY

Reference Number				R	an8

# COUNTRY of Guarantee

Country code				R	a2

# IE035. Recovery notification  E_REC_NOT

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

COMPETENT AUTHORITY for Recovery	1 x	R

TRADER Principal	1 x	R

GUARANTOR	1 x	O

# TRANSIT OPERATION

MRN						R	an18

Declaration Acceptance date		R	n8

Recovery notification text		O	an..350

Recovery_notification_text_LNG	O	a2	Rule 99

Recovery notification date		R	n8

Amount claimed				R	n..15,2

Currency					R	an3

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# COMPETENT AUTHORITY for Recovery

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				R	an..35

Street and number (box 50)		R	an..35

Country (box 50)				R	a2

Postcode (box 50)				R	an..9

City (box 50)				R	an..35

NAD_LNG					O	a2	Rule 99

# GUARANTOR

TIN						O	an..17	Rule 12

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# IE037. Response query on guarantees  C_GUA_RSP

GUARANTEE REFERENCE	99 x	R

GUARANTEE QUERY	1 x	R

USAGE	9999 x	C	Cond 280

EXPOSURE	1 x	C	Cond 285

TRADER Principal (owner)	1 x	C	Cond 270

GUARANTOR	1 x	C	Cond 234

GUARANTOR OTHER ADDRESSES	99 x	C	Cond 270

COMPREHENSIVE GUARANTEE	1 x	C	Cond 270

Rule 280		GOODS ITEM	99 x	C	Cond 235

VALIDITY LIMITATION EC	1 x	O

VALIDITY LIMITATION NON EC	99 x	O

INDIVIDUAL GUARANTEE BY GUARANTOR	1 x	C	Cond 270

Rule 280

GOODS ITEM	99 x	R

CUSTOMS OFFICE OF DEPARTURE	1 x	R

CUSTOMS OFFICE OF DESTINATION	1 x	R

VALIDITY LIMITATION EC	1 x	O

VALIDITY LIMITATION NON EC	99 x	O

INDIVIDUAL GUARANTEE VOUCHER	1 x	C	Cond 270

Rule 280

AUTHORITY FOR GUARANTEE SIMPLIFICATION	1 x 	O	Rule 265

CUSTOMS OFFICE (requester)	1 x	O	Rule 265

TRADER Principal (requester)	1 x 	O	Rule 265

OFFICE OF RECOVERY	1 x	O	Rule 265

CUSTOMS OFFICE of Guarantee	1 x	R

# GUARANTEE REFERENCE

GRN						R	an..24

Acceptance date				R	n8

Guarantee type				R	an1

Guarantee Monitoring code		R	n1

# GUARANTEE QUERY

Query identifier				R	n1

Period from date				C	n8	Cond 226

Period to date				C	n8	Cond 226

# USAGE

MRN						R	an18

Covered amount				R	n..15,2

Currency					R	an3	Rule 267

Lock date					R	n8

Arrival date					O	n8	Rule 264

Date of release				O	n8

# EXPOSURE

Exposure					R	n..15,2

Exposure counter				R	n..8

Balance					C	n..15,2	Cond 286

Currency					R	an3	Rule 267

# TRADER Principal (owner)

Trader Principal TIN			R	an..17	Rule 12

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

GUARANTOR

TIN						O	an..17	Rule 12

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

Contact person				O	an..35

Phone number				O	an..35

Fax number					O	an..35

Telex number				O	an..35

E-Mail Address				O	an..70

Language code				O	a2

# GUARANTOR OTHER ADDRESSES

Address type				R	a1

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

Contact person				O	an..35

Phone number				O	an..35

Fax number					O	an..35

Telex number				O	an..35

E-Mail Address				O	an..70

Language code				O	a2

# COMPREHENSIVE GUARANTEE

Reference amount				C	n..15,2	Cond 231

Percentage of reference amount		C	n..3	Cond 231									Rule 269

Guarantee amount				O	n..15,2	Rule 271

Currency					R	an3	Rule 267

Number of certificates			R	n..8

Validity date				R	n8

Invalidity date				O	n8

Invalidity reason code			O	an3

Invalidity reason				O	an..350

Invalidity_reason_LNG			O	a2	Rule 99

Liability liberation date			O	n8

Limited validity (sensitive goods)	R	n1	Rule 230

Restricted use (suspended goods)	R	n1	Rule 230

# INDIVIDUAL GUARANTEE BY GUARANTOR

Guarantee amount				R	n..15,2

Currency					R	an3	Rule 267

# GOODS ITEM

Textual Description			R	an..280

Textual_Description_LNG		O	a2	Rule 99

Commodity code				C	an..6	Cond 230

Sensitive goods code			O	n..2	Rule 156

# CUSTOMS OFFICE OF DEPARTURE

Reference Number				R	n8

# CUSTOMS OFFICE OF DESTINATION

Reference Number				R	n8

# VALIDITY LIMITATION EC

Not valid for EC				R	n1	Rule 230

# VALIDITY LIMITATION NON EC

Not valid for other Contracting parties	R	a2	Rule 231

# INDIVIDUAL GUARANTEE VOUCHER

Date of issue				R	n8

Expiry date					R	n8

Hard copy given to Principal		R	n1	Rule 230

Limited validity (sensitive goods)	R	n1	Rule 230

TIR Carnet					R	n1	Rule 230

Voucher amount				C	n..15,2	Cond 232

Currency					C	an3	Cond 232

Rule 267

# AUTHORITY FOR GUARANTEE SIMPLIFICATION

Reference Number				R	an8

# CUSTOMS OFFICE (requester)

Reference Number				R	an8

# TRADER Principal (requester)

Trader Principal (requester) TIN	R	an..17

# OFFICE OF RECOVERY

Reference Number				R	an8

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# IE038. Response to Movement query  C_MVT_RSP

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE requester	1 x	R

C_AAR_SND	1 x	R	Rule 821

Rule 846

EN ROUTE EVENT	9 x	O	Rule 240

Rule 241

INCIDENT	1 x	O

TRANSHIPMENT	1 x	O

NEW CONTAINERS	99 x	O

NEW SEALS INFO (Box F)	1 x	O

NEW SEALS ID (Box F)	9999 x	R

CTL_CONTROL	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE of Departure

Reference Number				R	an8	Rule 901			Rule 904			Rule 905

# CUSTOMS OFFICE requester

Reference Number				R	an8	Rule 901

# C_AAR_SND

# EN ROUTE EVENT

Place						R	an..35

Place_LNG					O	a2	Rule 99

Country					R	a2

# INCIDENT

Incident flag					R	n1

Incident information(Box 56)		O	an..350

Incident_information_LNG		O	a2	Rule 99

Endorsement date (Box G)		O	n8

Endorsement authority (Box G)		O	an..35

Endorsement_authority_LNG		O	a2	Rule 99

Endorsement place (Box G)		O	an..35

Endorsement_place_LNG		O	a2	Rule 99

Endorsement Country (Box G)		O	a2

# TRANSHIPMENT

New transport means identity (Box 55)	O	an..27	Rule 190

New_transport_means_identity_LNG	O	a2	Rule 99

New transport means nationality (Box 55)	O	a2	Rule 190

Endorsement Date (Box F)		O	n8

Endorsement Authority (Box F)		O	an..35

Endorsement_Authority_LNG		O	a2	Rule 99

Endorsement Place (Box F)		O	an..35

Endorsement_Place_LNG		O	a2	Rule 99

Endorsement Country (Box F)		O	a2

# NEW CONTAINERS

New Container Number (Box 55)	O	an..11	Rule 190

# NEW SEALS INFO

New Seals Number (box F)		R	n..4

# NEW SEALS ID

New Seals Identity (box F)		R	an..20

New_Seals_Identity_LNG		O	a2	Rule 99

# CTL_CONTROL

Transit Operation State Type		R	an..3	Rule 605

Other Movement Information Response	O	an..350

Other_Movement_Information_Response_LNG	O	a2	Rule 99

# IE043. Unloading permission  E_ULD_PER

TRANSIT OPERATION	1 x	R	Rule 195

CTL_CONTROL	1 x	O

TRADER Consignor (Box 2)	1 x	C	Rule 10

Cond 26

TRADER Consignee (Box 8)	1 x	C	Rule 11

Cond 1

Cond 26

GOODS ITEM	999 x	C	Cond 27	     TRADER Consignor (ex Box 2)	1 x	O	Rule 10

TRADER Consignee (ex Box 8)	1 x	C	Rule 11

Cond 2

CONTAINERS (Box 31)	99 x	C	Cond 55

PACKAGES (Box 31)	99 x	R

SGI-CODES (Box 31)	9 x	O

PRODUCED DOCUMENTS/CERTIFICATES (Box 44)	99 x	C	Cond 901

SPECIAL MENTIONS (Box 44)	99 x	O

CUSTOMS OFFICE of Departure (Box C)	1 x	C	Cond 27

TRADER Principal (Box 50)	1 x	C	Cond 27

SEALS INFO (Box D)	1 x	C	Cond 26

SEALS ID (Box D)	9999 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

TRADER At Destination	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Declaration type (box 1)			C	an..5	Cond 27

Total number of items (box 5)		C	n..5	Cond 27

Total number of packages (box 6)	C	n..7	Cond 27

Country of dispatch (box 15a)		C	a2     	Cond 135

Cond 26

Destination country (box 17a)		C	a2     	Cond 140

Identity At Departure (box 18)		C	an..27	Cond 5

Cond 26

Rule 35

Identity_At_Departure_LNG		O	a2	Rule 99

Nationality at Departure (box 18)	C	a2	Cond 6

Rule 35

Container (box 19)				C	n1	Rule 230

Cond 27

Declaration Acceptance date		C	n8	Cond 27

Total gross mass 				C	n..11,3	Cond 27

# CTL_CONTROL

Continue unloading			R	n1	Rule 510

# TRADER Consignor

Name (box 2)				R	an..35

Street and number (box 2)		R	an..35

Country (box 2)				R	a2

Postcode (box 2)				R	an..9

City (box 2)					R	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 2)					O	an..17  	Rule 12

# TRADER Consignee

Name (box 8)				R	an..35

Street and number (box 8)		R	an..35

Country (box 8)				R	a2

Postcode (box 8)				R	an..9

City (box 8)					R	an..35

NAD_LNG					O	a2	Rule 99

TIN (box 8)					O	an..17  	Rule 12

# GOODS ITEM

Declaration type (ex box 1)		C	an..5	Cond 45

Country of dispatch (ex box 15a)	C	a2	Cond 135

Destination country (ex box 17a)	C	a2	Cond 140

Textual Description (box 31)		R	an..280

Textual_Description_LNG		O	a2	Rule 99

Item Number (Box 32)			R	n..5	Rule 5

Rule 7

Commodity code (Box 33)		C	an..6	Cond 15

Gross Mass (box 35)			O	n..11,3

Net Mass (box 38)				O	n..11,3

# TRADER Consignor

Name (ex box 2)				R	an..35

Street and number (ex box 2)		R	an..35

Country (ex box 2)				R	a2

Postcode (ex box 2)			R	an..9

City (ex box 2)				R	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 2)				O	an..17  	Rule 12

# TRADER Consignee

Name (ex box 8)				R	an..35

Street and number (ex box 8)		R	an..35

Country (ex box 8)				R	a2

Postcode (ex box 8)			R	an..9

City (ex box 8)				R	an..35

NAD_LNG					O	a2	Rule 99

TIN (ex box 8)				O	an..17  	Rule 12

# CONTAINERS

Container numbers (Box 31)		R	an..11

# SGI-CODES

Sensitive goods code (Box 31)		O	n..2

Sensitive Quantity (Box 31)		R	n..11,3

# PACKAGES

Marks & numbers of Packages (Box 31)	C	an..42	Cond 60

Marks_&_numbers_of_Packages_LNG	O	a2	Rule 99

Kind of packages (Box 31)		R	an..3

Number of Packages (Box 31)		C	n..5	Cond 60

Rule 21

Number of Pieces (Box 31)		C	n..5	Cond 60

PRODUCED DOCUMENTS/CERTIFICATES

Document Type (Box 44)		R	an..4	Cond 901

Document Reference (Box 44)		C	an..35  	Cond 902

Document_Reference_LNG		O	a2	Rule 99

Complement of information(Box 44)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

# SPECIAL MENTIONS

Additional information id (Box 44)	R	an..5

Export from EC (Box 44)		C	n1	Cond 75

Rule 75

Export from country (Box 44)		C	a2	Cond 75

Rule 75

# CUSTOMS OFFICE of Departure

Reference Number (Box C)		R	an8 	Rule 901

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17  	Rule 12

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				R	an..35

Street and number (box 50)		R	an..35

Country (box 50)				R	a2

Postcode (box 50)				R	an..9

City (box 50)				R	an..35

NAD_LNG					O	a2	Rule 99

# SEALS INFO

Seals Number (box D)			R	n..4

# SEALS ID

Seals Identity (box D)			R	an..20

Seals_Identity_LNG			O	a2	Rule 99

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8 	Rule 901

# TRADER At Destination

TIN						O	an..17	Rule 12

Name						C	an..35	Cond 160

Street and number				C	an..35	Cond 160

Country					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE044. Unloading Remarks  E_ULD_REM

TRANSIT OPERATION	1 x	R

UNLOADING REMARK (Box I)	1 x	R

SEALS INFO (Box I)	1 x	C	Cond 200

SEALS ID (Box I)	9999 x	O	Rule 206

GOODS ITEM	9999 x	C	Cond 210

CONTAINERS (Box 31)	99 x	C 	Cond 210

PACKAGES (Box 31)	99 x	C 	Cond 210

SGI-CODES (Box 31)	9 x	C 	Cond 210

Rule 155

PRODUCED DOCUMENTS/CERTIFICATES (Box 44)	99 x	C 	Cond 210

RESULTS OF CONTROL	1 x	C	Cond 210

Rule 211

CUSTOMS OFFICE Presentation Office	1 x	R

TRADER At Destination 	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Total number of items (box 5)		C	n..5	Cond 210

Total number of packages (box 6)	C	n..7	Cond 210

Identity At Departure (box 18)		C	an..27	Cond 210

Identity_At_Departure_LNG		O	a2	Rule 99

Nationality at Departure (box 18)	C	a2	Cond 210

Total gross mass (box 35)		C	n..11,3	Cond 210

# UNLOADING REMARK

Unloading Completion			R	n1	Rule 186

State of seals ok				O	n1	Rule 200

Rule 340

Unloading date (Box I)			R	n8

Conform (Box I)				R	n1	Rule 205

Unloading Remark				O	an..350

Unloading_Remark_LNG		O	a2	Rule 99

# SEALS INFO

Seals Number (box I)			R	n..4

# SEALS ID

Seals Identity (box I)			R	an..20

Seals_Identity_LNG			O	a2	Rule 99

# GOODS ITEM

Textual Description (Box 31)		O	an..280

Textual_Description_LNG		O	a2	Rule 99

Item Number (Box 32)			R	n..5

Commodity code (Box 33)		C	an..6	Cond 15

Gross Mass (box 35)			O	n..11,3

Net Mass (box 38)				O	n..11,3

# CONTAINERS

Container numbers (Box 31)		R	an..11

# SGI-CODES

Sensitive goods code (Box 31)		O	n..2	Rule 156

Sensitive Quantity (Box 31)		R	n..11,3

# PACKAGES

Marks & numbers of Packages (Box 31)	C	an..42	Cond 60

Marks_&_numbers_of_Packages_LNG	O	a2	Rule 99

Kind of packages (Box 31)		R	an..3

Number of Packages (Box 31)		C	n..5	Cond 60

Rule 21

Number of Pieces (Box 31)		C	n..5	Cond 60

PRODUCED DOCUMENTS/CERTIFICATES

Document Type (Box 44)		R	an..4	Cond 901

Document Reference (Box 44)		C	an..35  	Cond 902

Document_Reference_LNG		O	a2	Rule 99

Complement of information (Box 44)	O	an..26

Complement_of_information_LNG	O	a2	Rule 99

# RESULTS OF CONTROL

Control indicator				R	an2

Description					O	an..140

Description_LNG				O	a2	Rule 99

Corrected value				O	an..27	Rule 150

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# TRADER at Destination

TIN						C	an..17	Cond 113

Name						C	an..35	Cond 160

Street and number				C	an..35 	Cond 160

Country					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# IE045. Write-off notification  E_WRT_NOT

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

GUARANTOR	1 x	O

# TRANSIT OPERATION

MRN						R	an18

Write-off date				R	n8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17	Rule 12

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				R	an..35

Street and number (box 50)		R	an..35

Country (box 50)				R	a2

Postcode (box 50)				R	an..9

City (box 50)				R	an..35

NAD_LNG					O	a2	Rule 99

# GUARANTOR

TIN						O	an..17	Rule 12

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# IE050. ATR  C_ATR_SND

TRANSIT OPERATION	1 x	R

C_AAR_SND	1 x	R	Rule 130

Rule 143

# TRANSIT OPERATION

Binding itinerary (Box D)		R	n1	Rule 230

# C_AAR_SND

# IE051. No release for Transit  E_REL_NOT

E_DEC_DAT	1 x	R	Rule 135

Rule 143

RESULTS OF CONTROL	1 x	O	Rule 145

CONTROL RESULT	1 x	R

TRANSIT OPERATION	1 x	R

# E_DEC_DAT

# RESULTS OF CONTROL

Control indicator				R	an2

Description					O	an..140

Description_LNG				O	a2	Rule 99

# CONTROL RESULT

Control date					R	n8

# TRANSIT OPERATION

MRN						R	an18

No Release Motivation			O	an..350

No Release Motivation_LNG		O	a2	Rule 99

# IE054. Request of release  E_REQ_REL

TRANSIT OPERATION	1 x	R

TRADER Principal	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of release request			R	n8

Release requested				R	n1	Rule 230

# TRADER Principal

Trader Principal TIN			O	an..17	Rule 174

Rule 12

Holder ID TIR				C	an..17	Cond 904

Name 					C	an..35	Cond 160

Street and number				C	an..35 	Cond 160

Country 					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE055. Guarantee not valid  E_GUA_INV

TRANSIT OPERATION	1 x	R

GUARANTEE REFERENCE	99 x	R

INVALID GUARANTEE REASON	1x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# GUARANTEE REFERENCE

GRN						R	an..24

# INVALID GUARANTEE REASON

Invalid Guarantee Reason Code		R	an..3

Error Text					O	an..350

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader PrincipalTIN (box 50)		O	an..17	Rule 12

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE058. Unloading remarks rejection  E_ULD_REJ

TRANSIT OPERATION	    1 x    R

UNLOADING REMARK	1 x	R

FUNCTIONAL ERROR 	999x 	O 	Rule 123

# TRANSIT OPERATION

# MRN	R	an18

# UNLOADING REMARK

Unloading remarks rejection date	R	n8

Unloading remarks Rejection reason	O	an..350

Unloading_remarks_Rejection_reason_LNG	O	a2	Rule 99

FUNCTIONAL ERROR

Error type 					R	 n2

Error pointer 				R 	an..210

Error reason 				O 	an..6

Original attribute value 			O 	an..140

# IE059. CANCEL ENQUIRY NOTIFICATION  C_CAN_ENQ

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE Requested	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Cancel enquiry notification date	R	n8

Cancel enquiry notification remarks	O	an..350

Cancel enquiry_notification_remarks_LNG	O	a2	Rule 99

CUSTOMS OFFICE of Departure

Reference Number				R	an8

CUSTOMS OFFICE Requested

Reference Number				R	an8

# IE060. Control decision notification  E_CTR_DEC

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of Control Notification		R	n8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN			O	an..17	Rule 12

Holder ID TIR				C	an..17	Cond 904

Name 					R	an..35

Street and number 				R	an..35

Country 					R	a2

Postcode 					R	an..9

City 						R	an..35

NAD_LNG					O	a2	Rule 99

# IE062. Release request rejection  E_REQ_REJ

TRANSIT OPERATION	1 x	R

FUNCTIONAL ERROR 	999x 	O 	Rule 123

# TRANSIT OPERATION

# MRN                                	             R       an18

Date of release request rejection	R	n8

Release request rejection reason	O	an..350

Release_request_rejection_reason_LNG	O	a2	Rule 99

FUNCTIONAL ERROR

Error type 					R	 n2

Error pointer 				R 	an..210

Error reason 				O 	an..6

Original attribute value 			O 	an..140

# IE063. recovery communication C_REC_COM

TRANSIT OPERATION	1 x	R	Rule 170

COMPETENT AUTHORITY of Country of Departure	1 x	R

CUSTOMS OFFICE of Destination	1 x	R

CUSTOMS OFFICE of Transit	9 x	O

# TRANSIT OPERATION

MRN						R	an18

Recovery Communication date		O	n8

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# CUSTOMS OFFICE of Destination

Reference Number				R	an8

# CUSTOMS OFFICE of Transit

Reference Number				R	an8

# IE070. Notification of System Unavailability to Common Domain  C_UNA_COM

COUNTRY	1 x	R

ACTION	9 x	R

SYSTEM UNAVAILABILITY	99 x	R

# COUNTRY

Country 					R	a2

# ACTION

Operation					R	a1	Rule 411

# SYSTEM UNAVAILABILITY

Business Functionality			R	a1

Downtime FROM				R	n12	Rule 660

System Unavailability Type		R	a1

Downtime TO				C	n12	Rule 660

Cond 400

Explanation					O	an..350

Explanation_LNG				O	a2	Rule 99

# IE071. Notification of System Unavailability to National Domain  C_UNA_NAT

COUNTRY	99 x	R

ACTION	9 x	R

SYSTEM UNAVAILABILITY	99 x	R

# COUNTRY

Country 					R	a2

# ACTION

Operation					R	a1	Rule 411

# SYSTEM UNAVAILABILITY

Business Functionality			R	a1

Downtime FROM				R	n12	Rule 660

System Unavailability Type		R	a1

Downtime TO				C	n12	Rule 660

Cond 400

Explanation					O	an..350

Explanation_LNG				O	a2	Rule 99

# IE100. Ask for documents  E_ASK_DOC

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	R

TRADER at Destination	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Ask for document text			R	an..350

Ask for document text _LNG		O	a2	Rule 99

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# TRADER At Destination

TIN						O	an..17	Rule 174

Rule 12

Name						C	an..35	Cond 160

Street and number				C	an..35	Cond 160

Country					C	a2 	Cond 160

Postcode					C	an..9 	Cond 160

City						C	an..35 	Cond 160

NAD_LNG					O	a2	Rule 99

# IE101. Return documents  E_DOC_SND

DOCUMENT	1 x	R

All documents related to the movement.

# IE102. Request on non-arrived movement  E_REQ_MOV

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of request on non-arrived movement	R	n8

Date limit for response			R	n8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# TRADER Principal

TIN (box 50)				O	an..17	Rule 174

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35	Cond 160

Country (box 50)				C	a2	Cond 160

Postcode (box 50)				C	an..9	Cond 160

City (box 50)				C	an..35	Cond 160

NAD_LNG					O	a2	Rule 99

# IE103. Information about non-arrived movement  E_MOV_RSP

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	C	Cond 215

Cond 315

TRADER Actual Consignee	1 x	C	Cond 215

ENQUIRY	1 x	R

TRADER Principal	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE Presentation Office

Reference Number				R	an8

# TRADER Actual Consignee

TIN						O	an..17

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# ENQUIRY

Date of Information received on non-arrived movement	R	n8

Information available			R	n1	Rule 230

TC11 delivered by Customs		R	n1	Rule 230

Rule 228

Delivery date				C	n8	Cond 220

# TRADER Principal

TIN (box 50)				O	an..17	Rule 174

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# IE104. Enquiry Request  C_ENQ_REQ

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Actual Consignee	1 x	O	Rule 505

ENQUIRY	1 x	R

REPLY TO REQUESTED ADDITIONAL INFORMATION	1 x	O	Rule 506

ADDITIONAL INFORMATION RESPONSE	99 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

CUSTOMS OFFICE requested	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Actual Consignee

TIN						O	an..17

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode 					R	an..9

City 						R	an..35

NAD_LNG					O	a2	Rule 99

# ENQUIRY

Enquiry date				R	n8

Information available			R	n1	Rule 230

TCR delivered by Customs		R	n1	Rule 230

Delivery date				C	n8	Cond 220

# REPLY TO REQUESTED ADDITIONAL INFORMATION

# ADDITIONAL INFORMATION RESPONSE

Additional Information Response Code	R	n2

Additional Information Response Text	C	an..140	Cond 320

Additional_Information_Response_LNG	O	a2	Rule 99

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# CUSTOMS OFFICE requested

Reference Number				R	an8

# IE105. Enquiry Reminder  C_ENQ_REM

C_ENQ_REQ	1 x	R

CUSTOMS OFFICE Higher authority of Destination	1 x	R

ENQUIRY	1 x	R

# C_ENQ_REQ

# CUSTOMS OFFICE Higher authority of Destination

Reference Number				R	an8

# ENQUIRY

Enquiry Reminder date			R	n8

# IE106. Enquiry response  C_ENQ_NEG

TRANSIT OPERATION	1 x	R

ENQUIRY	1 x 	R

REQUEST FOR ADDITIONAL INFORMATIONS	9 x	O

CUSTOMS OFFICE requested	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of enquiry response			R	n8

# ENQUIRY

Movement unknown at Destination	R	n1	Rule 250

Rule 230

Enquiry engaged at Destination		R	n1	Rule 250

Rule 230

Return Copy returned on			R	n8	Rule 251

# REQUEST FOR ADDITIONAL INFORMATION

Requested Additional Information Code	R	n1	Rule 251

Requested Additional Information Text	C	an..140	Cond 330

Requested_Additional_Information_LNG	O	a2	Rule 99

# CUSTOMS OFFICE requested

Reference Number				R	an8

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# IE110. Paper control results  C_RES_PAP

NCTS RETURN COPY	1 x	R	Rule 254

LIST OF ITEMS	1 x	O 	Rule 255

Rule 254

# NCTS RETURN COPY

# LIST OF ITEMS

# IE111. Authorised consignee query  C_AUT_QUE

CTL_CONTROL                                                                                     1 x    R		
TRADER Authorised Consignee	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE of Destination	1 x	R

# CTL_CONTROL

# Trader authorised NCTS                                                                    R       n1           Rule 230		Rule 17	Trader authorised TIR                                                                        R        n1	Rule 230		Rule 17

# TRADER Authorised Consignee

TIN						C	an..17	Cond 37

Holder ID TIR				C	an..17	Cond 37

Name						O	an..35

Street and number				O	an..35

Country					O	a2

Postcode					O	an..9

City						O	an..35

NAD_LNG					O	a2	Rule 99

# CUSTOMS OFFICE Of Departure

Reference Number				R	an8

# CUSTOMS OFFICE Of Destination

Reference Number				R	an8

# IE112. Response to Authorised consignee query C_AUT_RSP

CTL_CONTROL	1 x	R

TRADER Authorised Consignee	1 x	R

AUTHORISED GOODS LOCATION	99 x	C	Cond 290

AUTHORISED GOODS LOCATION LSD	9 x	R

CUSTOMS OFFICE of Destination	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# CTL_CONTROL

Trader authorised 				R	 n1	Rule 230

# TRADER Authorised Consignee

TIN						C	an..17	Cond 37

Holder ID TIR				C	an..17	Cond 37

Name						O	an..35

Street and number				O	an..35

Country					O	a2

Postcode					O	an..9

City						O	an..35

NAD_LNG					O	a2	Rule 99

# AUTHORISED GOODS LOCATION

Arrival Authorised Location Of Goods	R	an..17

# AUTHORISED GOODS LOCATION LSD

Language code				R	a2

Name						R	an..35

Street and Number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# CUSTOMS OFFICE of Destination

Reference Number				R	an8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE114. ATR Request  C_ATR_REQ

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Actual Office of Transit	1 x	R

COUNTRY of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE Actual Office of Transit

Reference Number				R	an8

# COUNTRY of Departure

Country code				R	a2

# IE115. ATR Response  C_ATR_RSP

TRANSIT OPERATION	1 x	O	Rule 216

C_ATR_SND	1 x	O	Rule 216

Rule 821

Rule 846

CUSTOMS OFFICE of Departure	1 x	O	Rule 216

CUSTOMS OFFICE Actual Office of Transit	1 x	R

# TRANSIT OPERATION

MRN						R	an18

ATR rejection reason code		R	n..2

ATR rejection reason			C	an..350	Cond 340

ATR_rejection_reason_LNG		O	a2	Rule 99

# C_ATR_SND

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# CUSTOMS OFFICE Actual Office of Transit

Reference Number				R	an8		Guarantee not valid for country		R	n1	Rule 230

# IE118. NCF  C_NCF_NOT

TRANSIT OPERATION	1 x	R

PASSAGE	1 x	R

CUSTOMS OFFICE Actual Office of Transit	1 x	R

EN ROUTE EVENT	9 x	O	Rule 240

INCIDENT	1 x	O

TRANSHIPMENT	1 x	O

NEW CONTAINERS	99 x	O

NEW SEALS INFO (Box F)	1 x	O

NEW SEALS ID (Box F)	9999 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# PASSAGE

Date of Passage				R	n8

# CUSTOMS OFFICE Actual Office of Transit

Reference Number				R	an8

# EN ROUTE EVENT

Place						R	an..35

Place_LNG					O	a2	Rule 99

Country					R	a2

# INCIDENT

Incident flag					R	n1	Rule 230

Incident information (Box 56)		O	an..350

Incident_information_LNG		O	a2	Rule 99

Endorsement date (Box G)		O	n8

Endorsement authority (Box G)		O	an..35

Endorsement_authority_LNG		O	a2	Rule 99

Endorsement place (Box G)		O	an..35

Endorsement_place_LNG		O	a2	Rule 99

Endorsement Country (Box G)		O	a2

# TRANSHIPMENT

New transport means identity (Box 55)	O	an..27	Rule 190

New_transport_means_identity_LNG	O	a2	Rule 99

New transport means nationality (Box 55)	O	a2	Rule 190

Endorsement date (Box F)		O	n8

Endorsement authority (Box F)		O	an..35

Endorsement_authority_LNG		O	a2	Rule 99

Endorsement place (Box F)		O	an..35

Endorsement_place_LNG		O	a2	Rule 99

Endorsement Country (Box F)		O	a2

# NEW CONTAINERS

New container number (Box 55)	O	an..11	Rule 190

# NEW SEALS INFO

New Seals Number (box D)		R	n..4

# NEW SEALS ID

New Seals Identity (box D)		R	an..20

New_Seals_Identity_LNG		O	a2	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE119. DEPARTURE control DOCUMENT on paper  E_DEP_PAP

DEPARTURE CONTROL DOCUMENT	1 x	R	Rule 256

# DEPARTURE CONTROL DOCUMENT

# IE120. DESTINATION control DOCUMENT on paper  E_DES_PAP

DESTINATION CONTROL DOCUMENT	1 x	R	Rule 257

# DESTINATION CONTROL DOCUMENT

# IE140 Request on non-arrived movement  E_REQ_MOV

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

TRADER Principal	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of request on non-arrived movement	R	n8

Date limit for response			R	n8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17	Rule 174

Rule 12

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35	Cond 160

Country (box 50)				C	a2	Cond 160

Postcode (box 50)				C	an..9	Cond 160

City (box 50)				C	an..35	Cond 160

NAD_LNG					O	a2	Rule 99

# IE141 Information about non-arrived movement  E_MOV_RSP

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE Presentation Office	1 x	C	Cond 215

Cond 315

TRADER Actual Consignee	1 x	C	Cond 215

ENQUIRY	1 x	R

TRADER Principal	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE Presentation Office

Reference Number				C	an8

# TRADER Actual Consignee

TIN						O	an..17

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# ENQUIRY

Information (on paper) available	R	n1	Rule 230

Information text				C	an..140	Cond 7

Information text_LNG			O	a2	Rule 99

TC11 delivered by Customs		R	n1	Rule 230

Rule 228

Delivery date information / TC11	C	n8	Cond 220

# TRADER Principal

Trader Principal TIN (box 50)		O	an..17	Rule 174

Holder ID TIR				C	an..17	Cond 904

Name (box 50)				C	an..35	Cond 160

Street and number (box 50)		C	an..35 	Cond 160

Country (box 50)				C	a2 	Cond 160

Postcode (box 50)				C	an..9 	Cond 160

City (box 50)				C	an..35 	Cond 160

NAD_LNG					O	a2 	Rule 99

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# IE142 Enquiry Request
C_ENQ_REQ

TRANSIT OPERATION	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

TRADER Actual Consignee	1 x	C	Cond 9

ENQUIRY	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R

CUSTOMS OFFICE requested	1 x	R

INFORMATION	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# TRADER Actual Consignee

TIN						O	an..17	Rule 12

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode 					R	an..9

City 						R	an..35

NAD_LNG					O	a2 	Rule 99

# ENQUIRY

Enquiry date				R	n8

TC11 delivered by Customs		R	n1	Rule 230

Delivery date information / TC11	C	n8	Cond 220

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# CUSTOMS OFFICE requested

Reference Number				R	an8

# INFORMATION
	Information (on paper) available 	R	n1	Rule 230

Information text				C	an..140	Cond 7

Information text_LNG			O	a2	Rule 99

Contact Person				O	an...140

Contact Person_LNG			O	a2	Rule 99

# IE143 Enquiry response
C_ENQ_NEG

TRANSIT OPERATION	1 x	R

ENQUIRY	1 x 	R

CUSTOMS OFFICE requested	1 x	R

COMPETENT AUTHORITY of Country of Departure	1 x	R	INFORMATION	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of enquiry response			R	n8

# ENQUIRY

Response Code				R	n..2

Return Copy returned on			C	n8	Cond 12

Response Information			C	an..140	Cond 13

Response_Information_LNG		O	a2	Rule 99

# CUSTOMS OFFICE requested

Reference Number				R	an8

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

# INFORMATION

Information (on paper) available	R	n1	Rule 230

Information text				C	an..140 	Cond 7

Information text_LNG			O	a2	Rule 99

Contact Person at Destination		O	an..140

Contact_Person at Destination_LNG	O	a2	Rule 99

# IE144 Enquiry & Recovery Information
C_ENR_INF

TRANSIT OPERATION	1 x	R

ENQUIRY	1 x 	R

ENQUIRY INFORMATION	99 x	R

COMPETENT AUTHORITY of Country of Destination 	1 x	R

COMPETENT AUTHORITY of Country of Departure 	1 x	R

CUSTOMS OFFICE of Departure	1 x	C	Cond 8

# TRANSIT OPERATION

MRN						R	an18

# ENQUIRY

Date of 'Enquiry Request' 		R	n8

Info from principal available		R	n1	Rule 230

# ENQUIRY INFORMATION

Information Code				R	n2	Rule 1

Information Text				C	an..140	Cond 320

Information_LNG				O	a2	Rule 99

# COMPETENT AUTHORITY of Country of Destination

Reference Number				R	an8

Contact Person				O	an..140
	Contact_Person_LNG			O	a2	Rule 99

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

Address					O	an..140

Address_LNG				O	a2	Rule 99

Contact Person				O	an..140
	Contact_Person_LNG			O	a2	Rule 99

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

Address					O	an..140

Address_LNG				O	a2	Rule 99

Contact Person				O	an..140
	Contact_Person_LNG			O	a2	Rule 99

# IE145 Enquiry & REcovery Information Request C_INF_REQ

TRANSIT OPERATION	1 x	R

ENQUIRY	1 x 	R

REQUEST FOR ENQUIRY INFORMATION	99 x	R

COMPETENT AUTHORITY of Country of Destination 	1 x	R

COMPETENT AUTHORITY of Country of Departure 	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# ENQUIRY

Date of 'Enquiry Request'			R	n8

# REQUEST FOR ENQUIRY INFORMATION

Requested Information Code		R	n1	Rule 2

Requested Information Text		C	an..140	Cond 330

Requested_ Information_Text_LNG	O	a2	Rule 99

# COMPETENT AUTHORITY of Country of Destination

Reference Number				R	an8

Reply Address				O	an..140

Reply_Address_LNG			O	a2	Rule 99

Contact Person				O	an..140
	Contact_Person_LNG			O	a2	Rule 99

# COMPETENT AUTHORITY of Country of Departure

Reference Number				R	an8

Contact Person				O	an..140	
 Contact_Person_LNG			O	a2	Rule 99

# IE150 Recovery Request
C_REC_REQ

TRANSIT OPERATION	1 x	R

RECOVERY	1 x	R

COMPETENT AUTHORITY of requesting Country	1 x	R

COMPETENT AUTHORITY of requested Country	1 x	R

INFORMATION	1 x	R

GUARANTEE INFORMATION                                                               99 x     C             Cond 4

GUARANTOR	1 x	C	Cond 14

# TRANSIT OPERATION

MRN						R	an18

# RECOVERY

Date of Recovery Communication	R	n8

# COMPETENT AUTHORITY of requesting Country

Reference Number				R	an8

# COMPETENT AUTHORITY of requested Country

Reference Number				R	an8

# INFORMATION

Information (on paper)			R	an..140

Information (on paper)_LNG		O	a2	Rule 99

Contact Person				O	an..140

Contact_Person_LNG			O	a2	Rule 99

# GUARANTEE  INFORMATION

# GRN                                                                                                   R       an..24

GUARANTOR

TIN						O	an..17	
	Guarantor name				R	an..35
	Guarantor street and number		R	an..35
	Guarantor place				R	an..35
	Postcode					R	an..9
	NAD_LNG					O	a2	Rule 99

Address etc. in country of competent authority	R	an..140

# IE151 Recovery Acceptance Notification C_REC_ACC

TRANSIT OPERATION	1 x	R

RECOVERY	1 x	R

COMPETENT AUTHORITY of requesting Country	1 x	R

COMPETENT AUTHORITY of requested Country	1 x	R

INFORMATION	1 x	O

GUARANTEE  INFORMATION                                                              99 x     C             Cond 25

GUARANTOR	1 x	C	Cond 14

# TRANSIT OPERATION

MRN						R	an18

# RECOVERY

Date of Recovery Communication	R	n8
	Acceptance					R	n1	Rule 230

# COMPETENT AUTHORITY of requesting Country

Reference Number				R	an8

# COMPETENT AUTHORITY of requested Country

Reference Number				R	an8

# INFORMATION

Information (on paper) available	O	n1	Rule 230
Information					R	an..140

Information_LNG				O	a2	Rule 99

Contact Person				O	an..140

Contact_Person_LNG			O	a2	Rule 99

GUARANTEE INFORMATION

GRN						R	an..24

GUARANTOR
	TIN						O	an..17

Guarantor name				R	an..35
	Guarantor street and number		R	an..35
	Guarantor place				R	an..35
	Postcode					R	an..9
	NAD_LNG					O	a2	Rule 99

Address etc. in country of competent authority	R	an..140

# IE152 Recovery Dispatch Notification
C_REC_DIS

TRANSIT OPERATION	1 x	R

RECOVERY	1 x	R

COMPETENT AUTHORITY of  County of Departure	1 x	R

COMPETENT AUTHORITY of  Country of Recovery	1 x	R

INFORMATION	1 x	O

# TRANSIT OPERATION

MRN						R	an18

# RECOVERY

Date of collection				R	n8

# COMPETENT AUTHORITY of  Country of Departure

Reference Number				R	an8

# COMPETENT AUTHORITY of  Country of  Recovery

Reference Number				R	an8

# INFORMATION

Information					R	an..140

Information_LNG				O	a2	Rule 99

Contact Person				O	an..140

Contact_Person_LNG			O	a2	Rule 99

# IE200. Guarantee check  C_GUA_CHE

TRANSIT OPERATION 	1 x	R

CUSTOMS OFFICE of Destination	1 x	C	Cond 233

GOODS ITEM	99 x	O	Rule 527

COUNTRY involved	99 x	R

CTL_CONTROL	1 x	O	Rule 526

TRADER Principal	1 x	R

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	R

CUSTOMS OFFICE of Departure	1 x	R

COUNTRY of Guarantee	1 x	C	Cond 227

# TRANSIT OPERATION

MRN						R	an18

Acceptance date				R	n8

# CUSTOMS OFFICE of Destination

Reference Number				R	an8

# GOODS ITEM

Commodity code				R	an..6

Sensitive goods code			O	n..2	Rule 156

# COUNTRY involved

Country (box 51 and box 53)		R	a2

# CTL_CONTROL

Sensitive goods flag			R	n1	Rule 230

Suspended goods flag			R	n1	Rule 230

# TRADER Principal

Trader Principal TIN			R	an..17

# GUARANTEE

Guarantee type (box 52)			R	an1

# GUARANTEE REFERENCE

GRN (box 52)				R	an..24

Access code					R	an4

Amount concerned				R	n..15,2

Currency					R	an3	Rule 267

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# COUNTRY of Guarantee

Country code				R	a2

# IE201. Guarantee check result  C_GUA_RES

TRANSIT OPERATION 	1 x	R

TRADER Principal	1 x	R

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	R

INVALID GUARANTEE REASON	9 x	O

CUSTOMS OFFICE of Guarantee	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# TRADER Principal

Trader Principal TIN			R	an..17

GUARANTEE

Guarantee type (box 52)			R	an1

# GUARANTEE REFERENCE

GRN (box 52)				R	an..24

# INVALID GUARANTEE REASON

Invalid Guarantee Reason Code		R	an..3

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE203. Guarantee use  C_GUA_USE

C_GUA_CHE	1 x	R

# C_GUA_CHE

# IE204. Guarantee use cancellation  C_GUA_CAN

TRANSIT OPERATION	1 x	R

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Date of usage cancellation		O	n8	Rule 515

Date of release				O	n8	Rule 515

# GUARANTEE

Guarantee type				R	an1

# GUARANTEE REFERENCE

GRN						R	an..24

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# IE205. Guarantee use result  C_GUA_USR

TRANSIT OPERATION 	1 x	R

TRADER Principal	1 x	R

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	R

VALIDITY LIMITATION EC	1 x	O

VALIDITY LIMITATION NON EC	99 x	O

INVALID GUARANTEE REASON	9 x	O

CUSTOMS OFFICE of Guarantee	1 x	R

CUSTOMS OFFICE of Departure	1 x	R

# TRANSIT OPERATION

MRN						R	an18

# TRADER Principal

Trader Principal TIN			R	an..17

GUARANTEE

Guarantee type (box 52)			R	an1

# GUARANTEE REFERENCE

GRN (box 52)				R	an..24

# VALIDITY LIMITATION EC

Not Valid For EC				R	n1	Rule 230

# VALIDITY LIMITATION NON EC

Not Valid For Other Contracting Parties	R	a2	Rule 231

# INVALID GUARANTEE REASON

Invalid Guarantee Reason Code		R	an..3

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# IE209. credit reference amount  C_GUA_Cre

TRANSIT OPERATION	1 x	R	Rule 268

GUARANTEE	9 x	R

GUARANTEE REFERENCE	99 x	R

CUSTOMS OFFICE of Departure	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

# TRANSIT OPERATION

MRN						R	an18

Arrival date					R	n8

# GUARANTEE

Guarantee type				R	an1

# GUARANTEE REFERENCE

GRN						R	an..24

# CUSTOMS OFFICE of Departure

Reference Number				R	an8

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# IE224. individual guarantee voucher sold  E_igv_INF

GUARANTEE REFERENCE	99 x	R

TRADER Principal	1 x	R

GUARANTOR	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

# GUARANTEE REFERENCE

GRN						R	an..24

Access code					R	an4

Date of issue				R	n8

Expiry date					R	n8

Hard copy given to Principal		R	n1	Rule 230

Limited validity (sensitive goods)	R	n1	Rule 230

TIR Carnet					R	n1	Rule 230

Voucher amount				C	n..15,2	Cond 232

Currency					C	an3	Cond 232

# TRADER Principal

Trader Principal TIN			R	an..17

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# GUARANTOR

TIN						O	an..17

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# IE225. Guarantee update notification  E_GUA_WUP

GUARANTEE REFERENCE	1 x	R	Rule 650

VALIDITY LIMITATION EC	1 x	O

VALIDITY LIMITATION NON EC	99 x	O

CUSTOMS OFFICE of Guarantee	1 x	R

TRADER Principal	1 x	R

# GUARANTEE REFERENCE

GRN						R	an..24

Reference amount				O	n..15,2

Percentage of reference amount		O	n..3

Guarantee amount				O	n..15,2

Currency					C	an3	Cond 350

Number of certificates			O	n..8

Validity date				O	n8	Rule 260

Invalidity date				O	n8	Rule 260

Invalidity reason code			O	an3

Invalidity reason 				O	an..350

Invalidity_reason_LNG			O	a2	Rule 99

Limited validity (sensitive goods)	R	n1	Rule 230

Restricted use (suspended goods)	R	n1	Rule 230

# VALIDITY LIMITATION EC

Not valid for EC				R	n1	Rule 230

# VALIDITY LIMITATION NON EC

Not valid for other Contracting parties	R	a2	Rule 231

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN			R	an..17

# IE228. Comprehensive guarantee cancellation liability liberation  E_GOG_CNL

GUARANTEE REFERENCE	1 x	R

TRADER Principal	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

GUARANTOR	1 x	R

# GUARANTEE REFERENCE

GRN						R	an..24

Guarantee amount				R	n..15,2

Currency					R	an3

Invalidity date				R	n8

Liability liberation date			R	n8

# TRADER Principal

Trader Principal TIN			O	an17

Name						R	an..35

Street and number				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# GUARANTOR

TIN						O	an..17

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# IE229. individual guarantee voucher revocation notification  E_IGV_RNG

GUARANTEE REFERENCE	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

GUARANTOR	1 x	R

# GUARANTEE REFERENCE

GRN						R	an..24

Invalidity date				R	n8

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# GUARANTOR

TIN						O	an..17

Name 					R	an..35

Street and number 				R	an..35

Country					R	a2

Postcode					R	an..9

City						R	an..35

NAD_LNG					O	a2	Rule 99

# IE231. Comprehensive guarantee cancellation notification  E_COG_CNP

GUARANTEE REFERENCE	1 x	R

CUSTOMS OFFICE of Guarantee	1 x	R

TRADER Principal	1 x	R

# GUARANTEE REFERENCE

GRN						R	an..24

Invalidity date				R	n8

Invalidity reason code			O	an3

Invalidity reason				O	an..350

Invalidity_reason_LNG			O	a2	Rule 99

# CUSTOMS OFFICE of Guarantee

Reference Number				R	an8

# TRADER Principal

Trader Principal TIN			R	an17

# IE410. Request for statistics  C_STA_REQ –  NO MORE DEFINED IN THIS DOCUMENT

# IE411. Sending of statistics data  C_STA_SND – NO MORE DEFINED IN THIS DOCUMENT

# IE412. Statistics generated sent to National Domain  C_STA_GEN -  NO MORE DEFINED IN THIS DOCUMENT

# IE413. OTS statistics sending to Common Domain  C_STA_OTS - NO MORE DEFINED IN THIS DOCUMENT

# CONDITIONS FOR IE

C1	 IF ‘Country of Destination’ (box 17a) on Transit Operation level 	contains one of the Contracting Parties, or AD or SM
		THEN	TRADER Consignee (box 8) = ‘R’
		ELSE		TRADER Consignee (box 8) = ‘O’.

Contracting parties are : 	the individual non EU countries of the  Convention on Common

Transit procedure and EU as a group.

C2	 IF ‘Country of Destination’ (ex box 17a) on GOODS ITEM level contains one of the Contracting Parties (see definition in C1), or AD or SM
		THEN	TRADER Consignee (ex box 8) = ‘R’
		ELSE		TRADER Consignee (ex box 8) = ‘O’.

C4	 IF the recovery request message is sent by country of departure AND 'Guarantee type' is 1, 2,

4 or 9,
		THEN	'GUARANTEE INFORMATION' = 'R'
		ELSE		'GUARANTEE INFORMATION' = 'O'.

C5	 IF first digit of ‘Inland mode of transport’ (box 26) = ‘5’ or ‘7’
		THEN	Identity at Departure (box 18) can not be used.

C6	 IF first digit of ‘Inland mode of transport’ (box 26) = ‘2’, ‘5’ or ‘7’
		THEN	‘Nationality at Departure’ (box 18) can not be used.

C7 	 IF 'Information (on paper) available' is '1' ('yes')
		THEN 	'Information text' = 'R'
		ELSE		'Information text' = can not be used.

C8	 IF the Competent Authority of the Country of Departure is equal to the Customs Office of Departure

THEN 	'CUSTOMS OFFICE of Departure' may not be used

ELSE 	'CUSTOMS OFFICE of Departure'= 'R'.

C9	 IF 'TRADER Actual Consignee' in IE141 is used
		THEN	'TRADER Actual Consignee' = 'R'
		ELSE		'TRADER Actual Consignee' = can not be used.

C10	 IF first digit of ‘Transport mode at the border’ (box 25) = ‘2’, ‘5’ or ‘7’ 
		THEN	‘Nationality crossing border’ (box 21) = ‘O’
		ELSE		‘Nationality crossing border’ (box 21) = ‘R’.

C11	 IF 'Nationality crossing border' is present or if 'Special circumstance indicator' is = 'D' 
		THEN	the attribute = 'R'
		ELSE		the attribute = 'O'.

C12 	 IF 'Response Code' = '3'
		THEN 	'Return Copy returned on' = 'R'
		ELSE		'Return Copy returned on' = can not be used

C13	 IF 'Response Code' = '2' or '4'
		THEN 	' Response Information' = 'R'
		ELSE 	'Response Information' = can not be used.

C14	 IF sending country is country of guarantee and if 'Guarantee type' is '1', '2', '4', or '9'
		THEN	'GUARANTOR' = 'R'
		ELSE		'GUARANTOR' = 'O'.

C15	 IF SGI-CODES is used
		THEN	‘Commodity Code’ (box 33) = ‘R’
		ELSE		‘Commodity Code’ (box 33) = ‘O’.

C25	 IF the recovery acceptance notification is sent by the country of departure AND 'ACCEPTANCE' flag is set to '1' (yes) AND (Guarantee type( is '1', '2', '4' or '9'
		THEN	'GUARANTEE INFORMATION' ( (R(
		ELSE		'GUARANTEE INFORMATION' ( (O(

C26	 IF the data group 'CTL_CONTROL' is present
		THEN	this data group/attribute can not be used
		ELSE

IF this data group/attribute is conditional based on others conditions
		THEN	these other conditions apply
		ELSE		this data group/attribute = 'O'

C27	 IF the data group 'CTL_CONTROL' is present
		THEN	this data group/attribute can not be used
		ELSE		this data group/attribute ='R'

C30	 IF there are different Contracting parties (see definition in C1) declared for Departure (identified by the Office of Departure, box C) and Destination (identified by the Office of Destination, box 53), or the country code of either Office of Departure or Destination is AD or SM
		THEN	at least one ‘CUSTOMS OFFICE of Transit’ (box 51) = ‘R’
		ELSE		‘CUSTOMS OFFICE of Transit’ (box 51) = ‘O’.

C35	 IF ‘Declaration type’ (box 1) or ‘Declaration type’ (ex box 1) = ‘T2’,’T2F’ and if the Country of the Office of Departure, identified by the first 2 digits of the ‘CUSTOMS OFFICE of Departure Reference Number’ (Box C) = is a non EU Contracting party
		THEN	‘PREVIOUS ADMINISTRATIVE REFERENCES’ = ‘R’
		ELSE		‘PREVIOUS ADMINISTRATIVE REFERENCES’ = ‘O’.

C37	 IF request / response concerns NCTS authorised consignee
		THEN	‘TRADER Authorised Consignee.TIN =’R’,

‘TRADER Authorised Consignee.Holder ID TIR’ can not be

used
		ELSE		‘TRADER Authorised Consignee.Holder ID TIR’=’R’

‘TRADER Authorised Consignee.TIN can not be used

C45	 IF ‘Declaration type’ (box 1) = ‘T-’
		THEN	‘Declaration type’ (ex box 1) = ‘R’ (T1, T2, T2F or T2SM)
		ELSE		‘Declaration type’ (ex box 1) can not be used.

C50	 IF ‘TIN’ (box 50) is used
		THEN	all attributes of name and address (NAD) (box50) = ‘O’ if

already known by NCTS
		ELSE		all attributes of name and address (NAD) (box50) = ‘R’.

C55	 IF ‘Container’ (box 19) = ‘1’
		THEN	‘CONTAINERS (box 31)’ must be present in at least one data 				group 'GOODS ITEM'
		ELSE		‘CONTAINERS (box 31)’ can not be used.

C60	 IF ‘Kind of packages’ (Box 31) indicates ‘BULK’ (UNECE rec 21 : ‘VQ’, ‘VG’, ‘VL’, ‘VY’,’VR’,'VS'  or ‘VO’)
		THEN	‘Marks & numbers of packages’ (Box 31) = ‘O’
				‘Number of packages’ (box 31) can not be used
				‘Number of Pieces’ (box 31) can not be used
		ELSE

IF ‘Kind of packages’ (Box 31) indicates ‘UNPACKED’ (UNECE rec 21 : = ‘NE’, 'NF' or

NG')
		THEN	‘Marks & numbers of packages’ (Box 31) = ‘O’

‘Number of packages’ can not be used

‘Number of Pieces’ (box 31) = ‘R’
		ELSE		‘Marks & numbers of packages’ (Box 31) = ‘R’

‘Number of packages’ (box 31) = ‘R’

‘Number of Pieces’ (box 31) can not be used.

C75	 IF ‘Additional Information id’ (Box 44) = ‘DG0’ or ‘DG1’
		THEN	‘Export from EC’ or ‘Export from country’ (Box 44) = ‘R’
		ELSE		‘Export from EC’ and ‘Export from country’ (Box 44) cannot

be used.

C85	 IF ‘Guarantee type’ = ‘0’, ‘1’, ‘2’, ‘4’,‘9’ or 'B'
		THEN	‘GUARANTEE REFERENCE’ = ‘R’
		ELSE		‘GUARANTEE REFERENCE’ = ‘O’.

C86	 IF ‘Guarantee type’ = ‘0’, ‘1’, ‘2’, ‘4’ or ‘9’, 
		THEN	‘Access code’ = ‘R’
		ELSE		‘Access code’ = ‘O’.

C90	 IF first digit of ‘Control result code’ = ‘B’
		THEN	‘Waiting for discrepancies resolution’ = ‘R’
		ELSE		‘Waiting for discrepancies resolution’ = ‘O’.

C100	 IF ‘CONTROL RESULT’ (Box D) is used
		THEN	‘Authorised location of goods’ = ‘O’
				‘Customs sub place’ can not be used
				‘Agreed location code’ can not be used
				‘Agreed location of goods’ can not be used
		ELSE		‘Authorised location of goods’ can not be used
				‘Agreed location code’ = ‘O’
				‘Agreed location of goods’ = ‘O’
				‘Customs sub place’ = ‘O’.

C111	 IF ‘CONTROL RESULT’ is present (Simplified procedure) or

IF 'Specific circumstance indicator 'E' is present and the first two digits of CUSTOMS OFFICE.Office of Departure consist of an EU Member State country code 
		THEN	‘TIN’ = ‘R’
		ELSE		‘TIN’ = ‘O’.

C112	 IF ‘CONTROL RESULT’ is present (Simplified procedure) or

IF the first two digits of 'CUSTOMS OFFICE of Destination.Reference number' consist of an EU Member State country code 
		THEN	‘TIN’ = ‘R’
		ELSE		‘TIN’ = ‘O’.

C113	 IF the first two digits of 'CUSTOMS OFFICE of Destination.Reference number' consist of an EU Member State country code 
		THEN	‘TIN’ = ‘R’
		ELSE		‘TIN’ = ‘O’.

C125	 IF ‘guarantee type’ = ‘0’, ‘1’, ‘2’, ‘4’ or ‘9’	
		THEN	‘GRN’ = ‘R’
		ELSE		‘GRN’ can not be used.

C130	 IF ‘GRN’ is NOT used
		THEN	‘Other guarantee reference’ = ‘R’
		ELSE		‘Other guarantee reference’ can not be used.

C135	 IF only 1 Country of dispatch is declared
		THEN	‘Country of dispatch (box 15a)’ on TRANSIT OPERATION

level = ‘R’, ‘Country of dispatch (ex box 15a)’ on

GOODS ITEM level cannot be used
		ELSE		‘Country of dispatch (box 15a)’ on TRANSIT OPERATION

level cannot be used, ‘Country of dispatch (ex box 15a)’ on

GOODS ITEM level = ‘R’.

C140	 IF only 1 Country of destination is declared
		THEN	‘Destination country (box 17a)’ on TRANSIT OPERATION

level = ‘R’, ‘Destination country (ex box 17a)’ on

GOODS ITEM level cannot be used
		ELSE		‘Destination country (box 17a)’ on TRANSIT OPERATION

level cannot be used, ‘Destination country (ex box 17a)

GOODS ITEM level = ‘R’.

C155	 IF ‘Simplified procedure flag’ = ‘YES’
		THEN	‘Arrival agreed location of goods’ can not be used
				‘Arrival agreed location code’ can not be used
				‘Customs sub place’ can not be used
				‘Arrival authorised location of goods’ = ‘O’
		ELSE		‘Arrival authorised location of goods’ can not be used
				‘Customs sub place’ = ‘O’
				‘Arrival agreed location of goods’ = ‘O’
				‘Arrival agreed location code’ = ‘O’.

C160	 IF TIN of Trader is used
		THEN	all attributes marked with this Condition = ‘O’ if already

known by NCTS
		ELSE		all attributes marked with this condition = ‘R’.

C170	 IF ‘Cancellation initiated by Customs’ = ‘Yes’
		THEN	‘Cancellation Decision’ can not be used
		ELSE		‘Cancellation Decision’ = ‘R’.

C175	 IF ‘Cancellation initiated by Customs’ = ‘No’

AND ‘Cancellation Decision’ = ‘0’ (=N0))

OR (‘Cancellation initiated by Customs’ = ‘Yes’)
		THEN 	‘Cancellation Justification’ = ‘R’
		ELSE		‘Cancellation Justification’ = ‘O’.

C180	 IF ‘Cancellation initiated by Customs’ = ‘Yes’
		THEN 	‘Date of cancellation request’ can not be used
		ELSE		‘Date of cancellation request’ = ‘R’.

C185	 IF first digit of ‘Control result code’ = ‘A’

AND second digit of ‘Control result code’ = ‘1’ or ‘2’ (‘Satisfactory’ or ‘Considered satisfactory’)
		THEN 	All data groups and attributes marked with ‘Cond 185’ can not

be used
		ELSE		All data groups and attributes marked with ‘Cond 185’ = ‘R’

when relevant.

C186	 IF the attribute 'TRANSIT OPERATION.Security' is not present
		THEN	the data group/attribute can not be used 
		ELSE		the data group/attribute is by default = 'O', except where

additional conditions or rules for the same data group/attribute

imply something else.

C187	 IF the attribute 'TRANSIT OPERATION.Security' is set to '1'
		THEN	the data group 'TRADER Consignor – security' on TRANSIT

OPERATION level or TRADER Consignor – security' on

GOODS ITEM level must be present.

C188	 IF the attribute 'TRANSIT OPERATION.Security' is set to '1' and the attribute 'SPECIAL

MENTION.Additional information_id' = '10600' is used for at least one GOODS ITEM
		THEN	the data group 'TRADER Consignee - security' and

the data group 'GOODS ITEM.TRADER Consignee - security'

can not be used
		ELSE		the data group 'TRADER Consignee – security' on TRANSIT

OPERATION level or TRADER Consignee – security' on

GOODS ITEM level must be present.

C191	 IF the attribute 'TRANSIT OPERATION.Security' is set to '1'
		THEN	the data group/attribute must be present
		ELSE		the data group/attribute = 'O'.

C200	 IF ‘State of seals ok’ = ‘NO’
		THEN	SEALS INFO = ‘R’
		ELSE		SEALS INFO = ‘O’.

C210	 IF UNLOADING RESULT, ‘Conform’ = ‘YES’ (NO remarks)
		THEN	All data groups and attributes marked with ‘Cond 210’ cannot

be used
		ELSE		All data groups and attributes marked with ‘Cond 210’ = ‘R’

when relevant.

C215	 IF ENQUIRY.Information (on paper) available = ‘1’ (= yes)
		THEN	At least one of the data groups becomes ‘R’ 
		ELSE		the 2 data groups can not be used.

C220	 IF ENQUIRY.TC11 delivered by Customs = ‘1’ (= yes)
		THEN	‘Delivery date information/TC11’ = ‘R’ 
		ELSE		‘Delivery date information/TC11’ can not be used.

C226	 IF 'Query identifier' = '1' or '3 and Guarantee type ‘0’, ‘1’ or ‘9’
		THEN	'Period from date' and 'Period to date' = 'R'
		ELSE		'Period from date' and 'Period to date' can not be used.

C227	 IF ‘COUNTRY of guarantee’ is different from the country of the ‘requester’
		THEN	‘COUNTRY of guarantee’ = R
		ELSE		‘COUNTRY of guarantee’ = O.

C230	 IF ‘Guarantee type’ = ‘9’ (Individual guarantee with multiple usage)
		THEN	the attribute = R
		ELSE		the attribute = O.

C231	 IF ‘Guarantee type’ = ‘0’ or ‘1’
		THEN	the attribute = R
		ELSE		can not be used.

C232	 IF ‘TIR Carnet’ =’1’
		THEN	‘Voucher amount’ and ‘Currency’ = R
		ELSE		can not be used.

C233	 IF in at least one occurrence of "GUARANTEE" ‘Guarantee type’ = ‘2’
		THEN	‘CUSTOMS OFFICE of Destination’ = R
		ELSE		can not be used.

C234	 IF ‘Guarantee type = 1, 2, 4 or 9
		THEN	the data group is required
		ELSE		can not be used.

C235	 IF ‘Guarantee type = 9
		THEN	the attribute is required
		ELSE		can not be used.

C236	 IF attribute ‘GRN (Box 52)’ of data group ‘GUARANTEE REFERENCE’ is used
		THEN	the attribute = R
		ELSE		the attribute = O.

C270	 IF ‘Query identifier’ = '4' (General information only)
		THEN	data groups marked with this condition = 'R'
		ELSE		data groups marked with this condition can not be used.

C280	 IF ‘Query identifier’ = '2' (Exposure only) or '4' (General information only)
		THEN	USAGE can not be used
		ELSE		USAGE = 'R'.

C285	 IF ‘Query identifier’ = '1' (Usage only) or '4' (General information only) or

'Guarantee type' = ‘2’ or '4' 
		THEN	EXPOSURE can not be used
		ELSE		EXPOSURE = 'R'.

C286	 IF 'Guarantee Monitoring code' = '3'
		THEN	'Balance' = 'R'
		ELSE		'Balance' can not be used.

C290	 IF ‘Trader authorised’ = ‘1’ (authorised)
		THEN	AUTHORISED GOODS LOCATION = 'R'
		ELSE		AUTHORISED GOODS LOCATION can not be used.

C295	 IF ‘Variable Holiday Date’ and/or ‘Variable Season Date’ = ‘1’
		THEN	‘Year’ = ‘R’
		ELSE		‘Year’ can not be used.

C300	 IF ‘Operation’ = ‘C’ OR ‘U’
		THEN	All attributes marked with this condition = ‘R’
		ELSE		All attributes marked with this condition = ‘O’.

C305	 IF 'AAR-/AER-/Summary Declaration-/ Pre-Arrival item rejection reason code' = '4' (other)
		THEN	'AAR/AER/Summary Declaration rejection reason' = 'R'
		ELSE		'AAR/AER/Summary Declaration rejection reason' = 'O'.

C310	 IF ‘Amendment rejection motivation code’ = ‘?’ (other) *
		THEN	'Amendment rejection motivation text' = 'R'
		ELSE		'Amendment rejection motivation text' = ‘O’

*(To be defined at national level).

C312	 IF 'Diversion Rejection Code'/'Entry Rejection Motivation Code' = '4' (Other)
		THEN	'Diversion Rejection Text' = 'R'
		ELSE		‘Diversion Rejection Text' = 'O'.

C315	 IF ‘TC11 delivered by Customs’ = ‘1’ (Yes)
		THEN	‘CUSTOMS OFFICE Presentation Office’ = ‘R’
		ELSE		‘CUSTOMS OFFICE Presentation Office’ = ‘O’.

C320	 IF " Information Response Code" = "10", "40" or "50"
		THEN	'Additional Information Response Text' = 'R'
		ELSE		'Additional Information Response Text" cannot be used.

C330	 IF "Requested Information Code" =  "5" or "6"
		THEN	'Requested Information Text' = 'R'
		ELSE		'Requested Information Text' can not be used.

C340	 IF 'ATR rejection reason code' = '4' (other)
		THEN	'ATR rejection reason' = 'R'
		ELSE		'ATR rejection reason' = 'O'.

C350	 IF ‘Reference amount’ and or 'Guarantee amount' is used
		THEN	'Currency' = 'R'
		ELSE		'Currency' can not be used.

C400	 IF ‘Type’ = ‘S’ (Scheduled)
		THEN	‘Downtime TO’ = ‘R’
		ELSE		‘Downtime TO’ = ‘O’.

C410	 IF ‘Geo-Info Code’ contains “/” (i.e. the Customs office is situated at the frontier)
		THEN	Attribute ‘Nearest Office’ = “R”
		ELSE		Attribute ‘Nearest Office’ can not be used.

C501	 IF the attribute 'TIN' is present in the data group 
		THEN	this attribute cannot be used
		ELSE		this attribute = 'R'.

C531	 IF 'Security' = '1' and Transport mode at border' = '4'
		THEN	the attribute is 'R' and consists of the (IATA/ICAO) flight

number and 	has format an..8:

-an..3: mandatory prefix identifying the airline/operator

-n..4: mandatory number of the flight

-a1: optional suffix
		ELSE		the attribute is 'O' and the format of the attribute has no

restrictions.

C547	 IF the attribute 'TRANSIT OPERATION.Security' is not present or if the 'Specific circumstance indicator' = 'A' ('TRANSIT OPERATION.Security' is present)
		THEN	the attributes 'Commercial Reference Number (box 7)',

'Commercial Reference Number (ex box 7)' and the data group

'PRODUCED DOCUMENTS/CERTIFICATES' = 'O'
		ELSE ('Security' is present and 'Specific circumstance indicator' not present

or other than 'A')

IF the attribute 'Commercial Reference  Number (box 7)' and 'Commercial Reference Number (ex box 7)' is not used
		THEN	at least one attribute 'PRODUCED DOCUMENTS/

CERITIFICATES.Document type' for the first GOODS ITEM

pointing to a transport document must be present
		ELSE		the data group 'PRODUCED DOCUMENTS/

CERTIFICATES' = 'O'

C572	 IF the attribute 'Specific circumstance indicator = 'E'

IF the first two digits of the CUSTOMS OFFICE.Office of Departure consist of an Member

State country code
		THEN	the attribute = 'R'
		ELSE		the attribute = 'O'
		ELSE		the attribute = 'O'

C576	 IF the attribute 'EXPORT OPERATION/IMPORT OPERATION/

TRANSIT OPERATION.Transport charges – Method of payment' is used
		THEN	this attribute can not be used
		ELSE		this attribute = 'O'.

C587	 IF the attribute 'Security' on HEADER level is present,
		THEN	the datagroup/attribute  = 'R'
		ELSE		the datagroup/attribute cannot be used.

C589	 IF the attribute 'Specific circumstance indicator' = 'B' or 'E' 
		THEN	the attribute 'Unloading place' = 'O'
		ELSE		the attribute 'Unloading place' = 'R'.

C596	 IF the attribute 'Specific circumstance indicator = 'E'

IF the first two digits of the 'CUSTOMS OFFICE of Departure.Reference number' do not consist of an Member State country code
		THEN	the attribute = 'R'
		ELSE		the attribute = 'O'
		ELSE		the attribute = 'O'.

C598	 IF the attribute 'TRANSIT OPERATION.Security = '1' and

the first two digits of the CUSTOMS OFFICE of Transit.Reference number consists of

a Member State country code and

the first two digits of the CUSTOMS OFFICE of Departure.Reference number does not consist

of an Member State country code
		THEN	the attribute = 'R'
		ELSE		the attribute = 'O'.

C599	 IF the attribute 'TRANSIT OPERATION.Security = '1' and

the first two digits of the CUSTOMS OFFICE of Departure.Reference number does not consist

of an Member State country code
		THEN	the attribute = 'R'
		ELSE		the attribute = 'O'.

C900	 IF "Declaration Type (box 1)" = 'TIR',
		THEN	"Type of Guarantee" type 'B' = 'R'
		ELSE		"Type of Guarantee" type 'B' cannot be used.

C901	 IF "Declaration Type (box 1)" = 'TIR',
		THEN	one occurrence of the value '952' of "Document Type

(box 44)"- irrespective of other document types declared –

must be entered within one operation and it must be present

in the first goods item
		ELSE		value '952' of "Document Type (box 44)" can not be used

C902	 IF "Document Type (box 44)" = '952',
		THEN	"Document Reference (box 44)" = 'R'
		ELSE		"Document Reference (box 44)" = 'O

C903	 IF "Declaration Type" = 'TIR',
		THEN	the data group 'PRODUCED DOCUMENTS/CERTIFICATES'

for the first Goods Item = 'R'
		ELSE		the data group 'PRODUCED DOCUMENTS/

CERTIFICATES' = 'O'

C904	 IF "Declaration Type" = 'TIR',
		THEN	"Holder ID TIR" = 'R',
		ELSE		"Holder ID TIR" can not be used.

# STRUCTURE RULES

R1	Each 'Enquiry Information Code' can only be used once per message.

R2	Each 'Requested Information Code' can only be used once per message.

R5	:‘Item no’ (box 32) is always used even if ‘Items’ (box 5) = ‘1’, ‘Item no’ (box 32) is also ‘1’.

R7	: Each ‘Item no’ (box 32) is unique throughout the declaration The items shall be numbered in a sequential fashion, starting from '1' for the first item and incrementing the numbering by '1' for each following item".

R10	: If the same Consignor/Exporter is declared for all goods items, the data group ‘TRADER Consignor (box 2)’/'TRADER Exporter (box 2)' on TRANSIT OPERATION/EXPORT OPERATION/IMPORT OPERATION level is used. The data group ‘TRADER Consignor (ex box 2)’/'TRADER Exporter (box 2)' on GOODS ITEM level can not be used.

R11	: When the same Consignee is declared for all goods items, the data group ‘TRADER Consignee (box 8)’ on TRANSIT OPERATION level is used. The data group ‘TRADER Consignee (ex box 8)’ on GOODS ITEM level can not be used.

R12	: The attribute is sent if it was provided in the corresponding message that was received from the Trader.

R15	: The data group ‘TRADER Authorised Consignee (box 53)’ can be used to indicate that simplified procedure will be used at destination.

R17	: Only one of the data attributes 'CTL_CONTROL.Trader authorised NCTS' and

'CTL_CONTROL.Trader authorised TIR' can be set to '1' (yes)

R20	: When the declaration type (box 1 or ex box 1) = ‘T2’ and the movement is issued in a non-EU country (identified by the Office of Departure), the Principal must declare at least one ‘Previous document type’ (box 40) = ‘T2’, ‘T2L’, ‘T2F’, ‘T2LF’, ‘T2CIM’, ‘T2TIR’ or ‘T2ATA’ followed by its reference in ‘Previous document reference’.

R21	:  A zero '0' is to be considered as a valid number in this field.

R27	: Either ‘Additional information id’ or ‘Text’ of the data group ‘SPECIAL MENTIONS’ (Box 44) is required in case ‘SPECIAL MENTIONS’ is used.

R35	: Conditions ‘C5’ and ‘C6’ can not be checked in case Box 26 is not used.

R36	: Condition ‘C10’ can not be checked in case Box 25 is not used.

R41	: ‘Agreed Location Of Goods’/’Agreed Location Code’, ‘Authorised location of goods’ and ‘Customs sub place’ (box 30) can not be used at the same time.

R60	: When the Trader uses Commodity codes then he must declare at least 4 and up to 8 digits of the commodity code.

R75	: ‘Export from EC‘ and ‘Export from country’ can not be used at the same time. When ‘Export from EC’ is used, its value is set to ‘1’.

R79	: The datagroups PREVIOUS ADMINISTRATIVE REFERENCES and PRODUCED DOCUMENTS/CERTIFICATES will be sent to Destination/Exit by means of IE001/501 only in case the declared attributes ‘Previous Document Type (Box 40)’ and/or ‘Document Type (Box 44)’ contain codes which are considered as ‘common’.

R80	: Only the SPECIAL MENTIONS that are marked as ‘Common’ in the reference data shall be

included in common domain messages.

R95	: The use of paper loading lists having been suppressed; this attribute can no longer be used.

R99	: This data item must be entered if the message is encoded in EDIFACT and the corresponding free text field is not in the UNOC character set. It is otherwise optional.

If the data item is filled in, it must contain the language code of the language used in the corresponding free text field.

R100	: The attribute is used as the basic language to be used in any further communication between the Trader and the Customs system. If the Trader does not use this attribute then the Customs system will use the default language of the Office concerned.

R101	: The attribute is used as the basic language to be used in any further communication between the Trader and the Customs system. If the Trader does not use this attribute then the Customs system will use the default language of the Office concerned.

R105	: The total number of packages is equal to the sum of all ‘Number of packages’ + all ‘Number of pieces’ + a value of ‘1’ for each declared ‘bulk’.

R115	: The IE structure used for the amendment is the same as 	E_DEC_DAT/E_EXP_DAT/E_EXS_DAT /E_ENS_DAT/E_SUD_DAT with some changes:
	replace LRN by MRN							R	an18,
	replace ‘Declaration date’ by ‘Date of amendment’		R	n8  (NCTS/ECS),

replace ‘Declaration date and time’ by ‘Date and time of amendment’  R	n12 (ICS),
	replace ‘Declaration place’ by ‘Amendment place’		R	an..35
The IE transmits a complete amended declaration data, this means that all data groups and attributes are transmitted and not only those that are amended.

R123	: From the originally received IE, only the attributes in error are transmitted back to the Trader, indicating whether the attribute(s) in question is (are) missing or incorrect.

R130	: When two or more Offices of Transit belong to the same National Administration and the IE50 is transmitted via EDI, then only one IE50 (ATR) is sent to the National Administration in question.

R135	: The IE retransmits back to the Trader the whole E_DEC_DAT received associating to each single attribute, when the case occurs, the data group ‘RESULTS OF CONTROL’.

R143	: The data in the IE corresponds always to the current (latest) version of the Transit/Export/Summary declaration operation data. This means that it contains the amended declaration data (if any) and/or the revised declaration data after a control (if any) and completed with the departure/export control results and entry/exit control results.

R145	: At least one occurrence of this data group must be present in the message.

R150	: The attribute ‘Corrected value’ of the data group ‘RESULTS OF CONTROL’ is linked with each single attribute that can be subject of a control and therefore it must reflect the same characteristics of the original message attribute.

R155	: The data group SGI-CODES must be present in case the declaration contains Sensitive Goods.

R156	: A ‘Sensitive Quantity’ is always required when the movement contains sensitive goods (see also Rule 155).
The ‘Sensitive Goods Code’ is not always required when the movement contains sensitive goods. If the HS6 commodity code (Box 33) is enough to uniquely identify a sensitive good then the ‘Sensitive Goods Code’ is not required. If the HS6 commodity code (Box 33) is not enough to uniquely identify a sensitive good then the ‘Sensitive Goods Code’ becomes required.

R157	: If the data group is present in the IE then at least one of the optional attributes must be filled in. When it concerns a data group containing a name/address then the attributes of the name/address are treated as one.

R160	: The data group CONTROL RESULTS must be present in case the declaration is submitted under simplified procedure.

R165	: The data group SEALS INFO must be present in case the declaration is submitted under simplified procedure, the authorisation of which foresees the use of seals.

R170	: This IE is only sent to the Offices of transit which have not notified that the consignment has crossed the frontier.
When the IE is transmitted via EDI and when two or more Offices of Transit belong to the same National Administration, or an (some) Office(s) of Transit and the Office of Destination belong to the same National Administration, then only one IE is sent to the National Administration in question.

R173	: When the IE10 is transmitted via EDI and two or more Offices of Transit belong to the same National Administration, or an (some) Office(s) of Transit and the Office of Destination belong to the same National Administration, then only one IE10 is sent to the National Administration in question.

R174	: When simplified procedure is used then the TIN becomes ‘R’ else the TIN is ‘O’.

R175	: Two possible values : 	‘0’ = ‘No’ : Request to cancel initiated by Trader
				‘1’ = ‘Yes’ : Request to cancel initiated by Customs.

R180	: Two possible values : 	Cancellation refused by Customs : Decision = ‘0’ (=NO)
				Cancellation accepted by Customs : Decision = ‘1’ (=YES)

R181	: The data group is required if different from the 'TRADER Principal' (otherwise it is optional).

R186	: ‘Unloading completion’ is used as a flag, it can contain 2 possible values;
‘0’ = ‘NO’ This means that the unloading of the goods is not yet completed;
‘1’ = ‘YES’ This means that the goods are completely unloaded.

R190	: Either ‘New transport means identity’ and ‘New transport means nationality’ OR ‘New container number’ OR both must be used when ‘TRANSHIPMENT’ occurred.

R195	: The purpose of this IE is to communicate the permission to start unload the goods (or to go on with the unloading) to the Authorised Consignee.

R200	: ‘State of seals ok’ is used as a flag and can contain 2 values:
		‘State of seals ok’ = ‘0’ (NO)
		‘State of seals ok’ = ‘1’ (YES).

R205	: ‘Conform’ is used as a flag, it can contain 2 possible values;
‘0’ = ‘NO’ there are unloading remarks;
‘1’ = ‘YES’ no unloading remarks present.

R206	: When no seals are found attached to the consignment and the information brought in by the AAR indicated the use of seals then SEALS ID can not be used, also, the attribute ‘Seals Number’ is set to zero and an explanation must be given in ‘Unloading Remark’ (=‘R’). In all other cases the data group SEALS ID is required.

R210	: The IE transmits to the Office of Departure/Office of Export the relevant AAR/AER information received from the Office of Departure/Office of Export associating to each single attribute, when the case occurs, the data group ‘RESULTS OF CONTROL’.

R211	: The IE retransmits back to the Customs Office of Destination the pertinent part of E_ULD_PER received associating to each single attribute, when the case occurs (this means when the attribute is incorrect), the data group ‘RESULTS OF CONTROL’.

R212	: The IE transmits to the Office of Departure/Export the relevant controlled declaration data associating to each single attribute, when the case occurs, the data group ‘RESULTS OF CONTROL’.

R213	: The IE is used to communicate the controlled items and minor or major discrepancies (if any).

R215	: Transit (NCTS):

'TRANSIT OPERATION'/'CUSTOMS OFFICE of Departure' and 'C_AAR_SND' cannot be used at the same time. When Customs can agree with the request for an AAR, the complete C_AAR_SND is sent to destination. When they disagree, only the MRN, CUSTOMS OFFICE of Departure (if rejection reason code is other than '3'), AAR rejection reason code and the AAR rejection reason (if necessary) are sent to destination.

Export declaration:

‘EXPORT OPERATION REJECTION’, ’CUSTOMS OFFICE of Export' and ‘C_AER_SND’ 	can not be used at the same time. When Customs can agree with the request for an AER,the 	complete 'C_AER_SND' is sent to exit. When they disagree, only the 'MRN', the 'CUSTOMS 	OFFICE of Export',the 'AER/ rejection reason code' and the 'AERrejection reason' (if 	necessary) are sent to exit.

Exit summary declaration:

‘EXPORT OPERATION REJECTION’, 'CUSTOMS OFFICE of Lodgement' and 	'C_EXS_SND' can not be used at the same time. When Customs can agree with the 	request for a Summary Declaration, the complete 'C_EXS_SND' is sent to exit. When 	they 	disagree, only the MRN, the CUSTOMS OFFICE of Lodgement, the 'Summary 	Declaration 	rejection reason code' and the 'Summary Declaration rejection reason' (if 	necessary) are sent 	to exit.

R216	: 'TRANSIT OPERATION'/'CUSTOMS OFFICE of Departure' and 'C_ATR_SND' can not be used at the same time. When Customs can agree with the request for an ATR, the complete C_ATR_SND is sent to Office of Transit. When they disagree, only the MRN, CUSTOMS OFFICE of Departure (if rejection reason code is other than '5'), ATR rejection reason code and the ATR rejection reason (if necessary) are sent to the Office of Transit.

R217	: All ‘Incidents’ occurred are transmitted to the Office of Departure. Only those ‘Transhipments’ marked ‘not yet sent’ (i.e. flag ‘Already in NCTS’ in the message ‘Arrival notification or a new box created for this purpose on the NCTS ACCOMPANYING DOCUMENT) are transmitted to the Office of Departure.

R228	: When the attribute 'Information available' is '0', the attribute "TC11 delivered by Customs" must have the same value.

R229	: The attribute is used to distinguish between cases where the NCTS is used (Security = '1') and not used (Security = not present) for safety and security purposes.

R230	: This attribute is used as a flag, its value can be either ‘0’ (‘no’) or ‘1’ (‘yes’).

R231	: The value of this attribute must be a country with the country regime 'TOC', with the exclusion of LI and SJ.

R232	: “Variable Holiday Date” and/or “Variable Season Date” are used as a flag and can contain 2 possible values:
‘0’: the holiday and/or season date is fixed and thus the year doesn’t have to be specified (e.g. Christmas = 25 December)
‘1’: the holiday and/or season date is variable and therefore the year will need to be specified together with the date (e.g. Easter Monday).

R240	: When the data group “EN ROUTE EVENT” is present then the data groups “INCIDENT” or “TRANSHIPMENT” or both must be present, complemented, where relevant, with the data group “NEW SEALS INFO”.

R241	: The datagroup “EN ROUTE EVENTS” is always required when information on “Incidents” and/or “Transhipments” are registered at OoDep.

R245	: “Customs sub place”, “Arrival authorised location of goods” and “Arrival Agreed Location Of Goods / Arrival Agreed Location Code” can not be used at the same time.

R250	: “Movement unknown at Destination” and ‘Enquiry engaged at Destination” can not be used at the same time.

R251	: This attribute is not to be used anymore (suppression of return copy).

R256	: This IE is always paper-based, it is used as a working document to perform a control of the goods (it is a print-out containing the accepted declaration data). During the control, the Customs Officer marks the control results on the paper.

R257	: This IE is always paper-based, it is used as a working document to perform a control of the goods at Destination/Exit/Entry (it is a print-out containing the received AAR/AER/E_EXP_SUM/EXS_DAT/E_ENS_DAT data). During the control, the Customs Officer marks the control results on the paper.

R260	: Either the guarantee is rendered invalid or it becomes again valid from a given date. ‘Invalidity date’ and ‘Validity date’ can not be used at the same time.

R261	: Query Identifier ‘2’ (exposure only) and ‘3’ (usage and exposure) can not be used for guarantee types ‘2’ (individual guarantee by Guarantor) and ‘4’ (individual guarantee in the form of voucher).

R262	: The data group can be used only when the query identifier code ‘4’ (general information only) is used.

R263	: The attribute can be used only with guarantee types ‘0’ (guarantee waiver), ‘1’ (comprehensive guarantee) or ‘9’ (Individual guarantee with multiple usage), with either Query Identifier ‘1’ (usage only) or ‘3’ (usage and exposure).

R264	: The attribute can be used only with guarantee types ‘0’ (guarantee waiver) and ‘1’ (comprehensive guarantee).

R265	: One of these data groups is the requester of the query. As a consequence one and only one data group must be present in the IE.

R266	: For international IEs, the data group can be used only when the query identifier code ‘4’ (general information only) is used.

R267	: For international IEs, the value of the attribute is always in EUR.

R268	: This IE can be used only with guarantee types ‘0’ (guarantee waiver) and ‘1’ (comprehensive guarantee).

R269	: This attribute is optional for international IEs.

R270	: When a Principal is requesting the information then the Access code (of the Principal) becomes required.

R271	: This attribute becomes optional for international IEs when guarantee type is ‘0’ or ‘1’, and is required in all other cases.

R275	: When the Principal requests information about the guarantee then data group ‘TRADER Principal (owner)’ and data group ‘TRADER Principal (requester)’ must have the same content, and the country of guarantee must be equal to the country of the ‘TRADER Principal (requester)’.

R280	: One and only one of the identified data groups must be present (required) in the IE.

R325	: When there are already seals identified in the AAR/AER and/or Arrival Notification/Arrival at Exit (IE507) then ‘State of seals’ is required.

R330	: The use of paper loading lists having been suppressed and all offices being NCTS offices, this data-group/attribute can no longer be used.

R335	: The data groups ‘CONTROL RESULT’ and where necessary ‘SEALS INFO’ become required only when a control by Customs took place at premises of the Authorised Consignor/Trader Exporter.

R340	: When the messages 43  E_ULD_PER and/or 7  E_ARR_NOT contain SEALS INFO then the ‘State of seals ok’ must be communicated.

R350	: The ‘old’ access code can be the same as the ‘new’ access code in case the Principal does not want to change his access code.

R355	: Only ‘GOODS ITEMS’ showing discrepancies are sent back to the Office of Departure/Export.

R403	: The seasonally opening days and hours periods are to be followed in succession, without any interruption in time. In other words: the ending day of the preceding period must be the day before the starting day of the following period. A time period of one year has to be covered.

R410	: The IE consists of top level data groups. Each top level data group has its own data group ACTION which attributes apply to the top level data group and its subsequent sub data groups.
The sender of the IE will always (in case of Create, Update and Delete) send all values of the occurrence.
The ‘Operation’ attribute is used to indicate what action is applied to the occurrence in the IE. Its value can be:
‘C’ (create) ,‘U’ (update), ‘D’(delete).
The ‘Validity date’ together with the attribute ‘Modification Subtype’ allow the following mechanism;
An occurrence becomes invalid as of the specified ‘Validity date’ when the value of ‘Modification Subtype’ is set to ‘0’ (implies an implicit end date).
An occurrence and all values of the attributes become valid as of the specified ‘Validity date’ when the value of ‘Modification Subtype’ is set to ‘1’.
  
‘C’ (create) : 
The create operation is used to create a new occurrence of an entity;
‘U’ (update). 
The update operation is used to change an existing occurrence. It can render an existing occurrence invalid or it can modify existing values of attribute(s) of an occurrence; 
‘D’ (delete). 
The delete operation is used to physically delete an occurrence. This operation must only be used when data has been created erroneously.

R411	: The ‘Operation’ attribute is used to indicate what action is applied:
‘C’ (create), ‘D’ (delete).
In case of “updates”, the data group ‘SYSTEM UNAVAILABILITY’ to be updated will be first deleted and then (re)-created.

R422 	: This attribute refers to the content of Column 2 in the UN/LOCODE. Column  2 shows the names of the locations (city names) which have been accepted for inclusion in UN/LOCODE, in accordance with the provisions of Recommendation n° 16 (see Rule 460).

R425 	: The attribute ‘Season Code’ is NOT used as a flag. It is possible to have up to 9 different ‘seasons’ in a year, depending on a defined time period, which is completely covering the year-period.

R430 	: The ‘Day in the week (end)’ must be equal or greater then the ‘Day in the week (begin)’.

R445	: 	The SENSITIVE GOODS CODE consists of two parts:  the first part represents the HS6 six digit commodity code of the TARIC system, the second part represents the  ‘Sensitive Goods Code’ which is a two numeric digit code,  defined by DG TAXUD.

This two digit numeric ‘Sensitive Goods Code’ is only used when the 6 digit HS6 code is not specific enough to identify the concerned goods (example: the codes ‘0405xx’ and ‘2208xx’ in the TARIC system cover both sensitive and non sensitive goods, or more than one sensitive good, and must be extended to 0405xx.01 and 2208xx.01 in order to uniquely identify the sensitive goods).

These codes are used in the ’’List of Goods which when transported give rise to an increase in the Flat-rate Guarantee” (see proper domain).

R450	: ‘Declaration Type’ (box 1 of SAD form) is split up into three subdivisions:

1st subdivision (declaration symbol): up to 3 alphabetic characters related to the type of movement concerned;

2nd subdivision (declaration type): one numeric code related to the type of procedure concerned;

3rd subdivision (declaration transit): up to 5 alphanumeric characters. Only this 3rd subdivision has to be considered in the context of this Transit application.

R456	: for ‘Package Code’ use the alphabetic two-digit UN-code going from ‘AE’ = ‘aerosol’ to ‘WB’ = ‘Wickerbottle’.

R460	: This UN/LOCODE refers to the 3 digit alphabetical code of the second part of Column 1 in the UN/LOCODE - Code for Ports and other Locations. Column 1 shows in a first part the ISO  3166  alpha-2 Country Code which is followed by a space and a 3-alpha code for the city (location) name: XX XXX. This combination is invariably identifying the ‘City Name’. This UN/LOCODE city name is used as an attribute in the ‘CUSTOMS OFFICE LSD’ entity.

R470	: The IE15 allows the usage of commodity codes up to 8 digits (national), however only the first six digits are sent to destination with the AAR (international) and to the Office(s) of Transit with the ATR (international).

R485	: Not all offices have a time-table, e.g. the Customs Offices that are HIGHER AUTHORITY. However when the Customs Offices are used by Traders then at least a time table should be provided.

R486	: This attribute can be used to indicate potential specific characteristics of the Customs Office, namely regarding variation of opening hours (e.g. during public holidays, etc.), operational and/or procedural restrictions (e.g. competent only for simplified procedures, competent only for certain goods, the only office authorised to accept flat-rate guarantees, etc.). This attribute will be coded by DG TAXUD after clear definition of the need of the NAs.

R489	: Reference Number Main Office is used to indicate the Customs Office (local) to which the Customs Office in question is subordinate. The use of this attribute is left up to the NAs.

R490	: Reference Number Higher Authority (see Compendium, Part 1, Title III, Chapter 3, Section 1, B.6.) is used to indicate that the Customs Office in question has a higher authority. As a consequence this attribute becomes required when the Office in question has a higher authority.

R495	: Reference Number Take-over is used to indicate another Customs Office that replaces (take-over) the Customs Office in question when the latter is no longer able to perform NCTS operations.

R500	: At least 1 of the 4 attributes must be present.

R505	: This data group is only filled in with the information received from the Principal at departure via IE103 (if any).

R506	: This data group is only used when the received IE106 contains the data group “REQUEST FOR ADDITIONAL INFORMATION”. In this case, IE104 (completed with the requested additional information) will be re-sent to ‘CUSTOMS OFFICE Requested’.

R510	: The attribute 'Continue unloading' of the data group CTL-CONTROL indicates with its progressive numbering, starting from 1, that the IE043 is transmitted to give the first or further permission to continue the unloading.

Where the IE brings the permission to start the unloading the data group CTL_CONTROL can not be used.

Where the IE communicates the permission to continue the unloading then only the attribute MRN of the data group TRANSIT OPERATION and the data groups CTL_CONTROL, CUSTOMS OFFICE Presentation Office and TRADER At Destination are used, all the other data groups and attributes can not be used.

R515	: Only one of the attributes 'Date of usage cancellation' and 'Date of release' must be present.

R520	: The IE is used for 2 different types of amendment:
IF the ‘Amendment Type Flag’ is ‘0’, then it is allowed to amend all items of the original declaration data, 
IF the ‘Amendment Type Flag’ is ‘1’, then it is only allowed to amend the original declared guarantee, i.e. the data groups GUARANTEE, GUARANTEE REFERENCE, VALIDITY LIMITATION EC and VALIDITY LIMITATION NON EC.

In both cases it is not allowed to amend the data groups TRADER Principal (Box 50) and CUSTOMS OFFICE of Departure (Box C).

R526	: This data group becomes mandatory when the declaration contains sensitive goods/suspended goods.

R527	: This data group becomes mandatory when the declaration contains commodity codes and when the guarantee type is ‘2’ (Individual guarantee by guarantor) or ‘9’ (Individual guarantee with multiple usage).

R605	: For an international IE038/538, the values of this attribute must be amongst those defined by the common domain (see IE032, data group ‘TRANSIT OPERATION STATE TYPE’/ EXPORT OPERATION STATE TYPE).

R610	: This attribute becomes mandatory when the IE is sent to the TRADER Principal, otherwise it can not be used.

R650	: At least one of the optional data sub groups or attributes must be filled in.

R660	: The time has to be given in the format YYYYMMDDHHMM where:
YYYY	= Year
MM		= Month
DD		= Day
HH		= Hour
MM		= Minute

R665	: The timestamp has to be given in the format YYYYMMDDHHMMSS where:

YYYY	= Year
MM		= Month
DD		= Day
HH		= Hour
MM		= Minute

SS		= Second

R700	: This information is not required when goods of different type covered by the same declaration are packed together in such a way that it is impossible to determine the gross mass of each type of goods.

R821	: Only those occurrences of the data group shall be included in the message for which the last digit of the attribute 'Risk Analysis result code' has one of the following values: D, E and Z.

R824	: The 'Item Number (box 32) involved' shall be indicated if the risk analysis result relates to an item of an Entry summary declaration (ICS), Exit summary declaration or Export declaration (ECS) or Transit declaration (NCTS). In any other case the attribute 'Item Number (box 32) involved' shall not be used.

R825	: The 'Specific circumstance indicator' with value 'E' (AEO) can be used only under following condition:

The Office of Departure is located in the Community: the 'Principal' and all declared 'Consignors-security' have a valid AEO certificate of type 'AEOF' or 'AEOS'.

The Office of Departure is not located in the Community: the 'Principal' and all declared 'Consignees-security' have a valid AEO certificate of type 'AEOF' or 'AEOS'.

R846: 	The content of the data group 'RISK ANALYSIS' shall only be sent if the requesting Customs Office is in the Community:

IE003: IE002.CUSTOMS OFFICE Presentation Office.Reference number

IE038: IE027. CUSTOMS OFFICE requester.Reference number,

IE115: IE114.CUSTOMS Office Actual Office of Transit.Reference number.

R876	: If the same 'Commercial reference number' is declared for all goods items, the attribute 'Commercial reference number' (box 7) on Export/Transit/Import Operation level is used. The attribute 'Commercial reference number' (ex box 7) on goods item level can not be used.

R900	: When "Declaration Type (box 1)" = 'TIR', the TIR Carnet Number must be used here, that shall correspond to the Document Reference of Document Type '952' in PRODUCED DOCUMENTS/CERTIFICATES.

R901	: When "Declaration Type (box 1)" = 'TIR', the country code (first two digits) in the code of OoDep/Des must have the country regime 'EEC'.

R902	: When "Declaration Type (box 1)" = 'TIR', CUSTOMS OFFICE of Transit cannot be used.

R903	: When "Declaration Type (box 1)" = 'TIR', Control Result Code 'A3' can not be used.

R904	: When Country of Dispatch is AD or SM, Destination Country can only be EEC.

R905	: Destination Country can not be AD or SM when Country of Dispatch is a non EU Contracting party.

R906	: When Destination Country is AD, the country code of Office of Transit can only be AD.

R907	: When Destination Country is SM, the country code of Office of Transit can only have the country regime EEC.

R908	: When Country of Dispatch is a non EU Contracting party,  Office of Transit can not have the country code AD or SM.

R909	: When the country code of Office of Destination (box 53) is 'SM' and the country code of Office of Departure (box C) is 'IT', declaration type (box 1) can only be 'T2SM'. When the country code of Office of Destination (box 53) is 'SM' and the country code of Office of Departure (box C) is not 'IT', declaration type (box 1) can only be 'T2' or T2F.

R910	: When Country of Dispatch is AD or SM, the country regime code of Office of Transit can only be EEC.

R911	: When the country code of the Office of Departure  is 'SM' and the country code of the Office of Destination is an EU country,  'Declaration type (box 1)'  can only be 'T2' or 'T2F'.

# Footnotes

Not to be used for movements released after 30.06.2009.

LSD stands for Language Specific Data.

Old enquiry message; not to be used for movements released after 30.06.2009.

Old enquiry message; not to be used for movements released after 30.06.2009.

Old enquiry message; not to be used for movements released after 30.06.2009.

New enquiry message; to be used for movements released after 30.06.2009.

New enquiry message; to be used for movements released after 30.06.2009.

New enquiry message; to be used for movements released after 30.06.2009.

New enquiry message; to be used for movements released after 30.06.2009.

New enquiry & recovery message; to be used for movements released after 30.06.2009.

New enquiry & recovery message; to be used for movements released after 30.06.2009.

New recovery message; to be used for movements released after 30.06.2009.

New recovery message; to be used for movements released after 30.06.2009.

New recovery message; to be used for movements released after 30.06.2009.

The document reference in case of Document Type '952' has to have the format an10 and must follow the algorithm used by the international organisation (Article 6.2 bis of the TIR Convention).

Recommendation n° 21/Rev. 2 adopted by the Working Party on Facilitation of International Trade Procedures

Recommendation n°16, second edition adopted by the Working Party on Facilitation of International Trade Procedures. - Geneva, January 1996.